## Slide 1
Air Quality Reanalysis
(Translating research to service)
13th CMAS Oct27-29, 2014, Chapel Hill
Pius Lee1, Greg Carmichael2, Yongtao Hu3, Edward Hyer4, Yang Liu5, Dick McNider6, Brad Pierce7 , Arastoo Pour Biazar6, Ted Russell3, Scott Spak2, Youhua Tang1,8, Hyuncheol Kim1,8,
Li Pan1,8, Weiwei Chen1,9 and Daniel Tong1,8
1Air Resources Lab., NOAA Center for Weather and Climate Prediction, College Park, MD
2College of Engineering, University of Iowa, Iowa City, IA
3School of Civil and Environmental Engr., Georgia Institute of Technology, Atlanta, GA
4Naval Research Laboratory, Monterey, CA
5Department of Environmental Health, Emory University, Atlanta, GA
6Department of Atmospheric Science, University Alabama, Huntsville AL
7National Environmental Satellite and Information Service (NESDIS), Madison, WI
8Cooperative Institute for Climate and Satellite, University of Maryland College Park, MD
9Northeast Institute of Geography and Agroecology, Chinese Academy of Sciences
Notes: Emphasis on teamwork: Overall team leadership provided by Professor Greg Carmichael.

## Slide 2
Constrained
Satellite
Products
Global
Assimilation
+ AQ Assessments
+ State Implementation Plan Modeling
+ Rapid deployment of on-demand rapid-response forecasting; e.g., new fuel type,…, etc.
+ Health Impacts assessments
+ Demonstration of the impact of observations on AQ distributions
+ Ingestion of new AQAST products into operations
http://acmg.seas.harvard.edu/aqast/projects.html
AQAST Project: Air Quality Reanalysis
(Translating Research to Services)
13th CMAS Oct27-29, 2014, Chapel Hill
Kim (Poster Tue16)
Notes: Objective: Best estimated state of the chemical composition of the atmosphere (lower troposphere)
A sizeable user group: AQ application as well as health epidemiology scenarios
A ‘reanalysis’ is a climate or weather model simulation of the past that includes data assimilation of historical observations. The observations can be very comprehensive (satellite, in situ, multiple variables) or relatively sparse (say, sea level pressure only), and the models themselves are quite varied. Generally these models are drawn from the weather forecasting community (at least for the atmospheric components) which explains the odd terminology. An ‘analysis’ from a weather forecasting model is the 6 hour (say) forecast from the time of observations. Weather forecasting groups realised a decade or so ago that the time series of their weather forecasts (the analyses) could not be used to track long term changes because their models had been updated many times over the decades. Thus the idea arose to ‘re-analyse’ the historical observations with a single consistent model. These sets of 6 hour forecasts using the data available at each point are then more consistent in time (and presumably more accurate) that the original analyses were. - See more at: http://www.realclimate.org/index.php/archives/2011/07/reanalyses-r-us/#sthash.WKOIKeHl.dpuf

## Slide 3
This study aims to build a prototype
User friendliness and reliability are keys to success: e.g..
Goal: A user friendly downloadable archive
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Long term – user, and on-demand subseting and downloading gui e.g.

## Slide 4
Applications of Reanalysis
Ozone – modeled (~ 3 yr data lag) & monitor (~ 1 yr data lag), both from EPA
PM2.5 mass - modeled (~ 3 yr data lag) & monitor (~ 1 yr data lag), both from EPA
Air Toxics - benzene, formaldehyde, modeled from EPA, 2005 only (NATA)
Reanalysis would be able to provide PM2.5 speciation data with national coverage at county level, which are highly valuable for health effects studies
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Tracking currently group their data into 4 categories. The first order application of our reanalysis data would be in the subcategory “Outdoor Air” under “Environments”.
The call out box shows what Tracking currently has and the data limitations
Second order application would be to provide more up to date air toxics data – needs further discussion to make it useful to Tracking.

## Slide 5
WRF_ARW-MCIP-CMAQ forward model
CMAQ 4.7.1
WRF-ARW (LCC)
(42 -P model Layers)
LBC from GFS
Projection of
endo-domain intermitten sources: Obs’d wild fire
and prescribed burns
EPA Emissions Inventory + simple obs-based adjustment
Hourly 3-D Gridded Chemical Concentration
MCIP
MODIS-
AOD-based adjusted IC,
BC: RAQMS
C-grid
C-grid
Column integrated AOD
C-grid
42 -P met. Layers
C-grid
C-grid
13th CMAS Oct27-29, 2014, Chapel Hill
Li (Poster Mon31)
Tong,Chen (Talks Wed)
McQueen
(Talk Tue)
Huang
(Poster Mon41)

## Slide 6
CMAQ4.7.1 | Both CONUS(12 km) & SENEX (4 km)
Map projection & grid | Lambert Conformal & Arakawa C staggering
Vert. co-ordinate | 42 σ-p unevenly spaced levels
Gas chemistry | Cb05 with 156 reactions
Aerosol chemistry | Aero5 with updated evaporation enthalpy
Anthropogenic emission | 2005NEI as base year, mobile projected using AQS*, area and off-road used CSPR^, point source uses 2012 CEM data
 | WRAP oil and gas emissions data
Biogenic emission | BEIS-3.14
Lateral BC | RAQM (B. Pierce)
42 vertical layers
WRF_ARW-MCIP-CMAQ model physics and chemistry options
WRF-ARW | Both North America (12 km) & CONUS (4 km)
Map projection & grid | Lambert Conformal & Arakawa C staggering
Vert. co-ordinate | 42 σ-p unevenly spaced levels
advection | RK3 (Skamarock and Weisman (2008))
SW & LW radiation | RRTMG (Iacono et al. 2008))
PBL Physics | Mellor-Yamada-Janjic (MYJ) level 2.5 closure
Surface layer scheme | Monin-Obukhov Similarity with viscous sub-layer
Land Surface Model | NCEP NOAH
Cloud Microphysics | Thompson et al. (2008)
Cloud convective mixing | Betts-Miller-Janjic Mass adjustment
AQ forecast: ^12 km nested to 4 km
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: ^12 km domain is set a bit large to match National AQ Forecasting Capability for side-by-side verification.

## Slide 7
Re-configuration of vertical structure: Decision to match GFS (NCEP)
sigma | Pres (hPa) | Z (m)
1 | 1013 | 0
0.999 | 1012 | 4
0.996 | 1010 | 20
0.992 | 1007 | 48
0.985 | 993 | 92
0.864 | 872 | 1245
0.843 | 852 | 1430
0.824 | 836 | 1590
0.808 | 821 | 1735
0.322 | 348 | 8150
0.297 | 326 | 8580
0.278 | 310 | 8940
0.262 | 296 | 8580
Near surface
Top of fully dev PBL
tropopause
13th CMAS Oct27-29, 2014, Chapel Hill

## Slide 8
Transmittance
AIRNow
Cloud-obs Photolysis rates
Isoprene
& PAR
done
done
done
Yet to do
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.
HMS

## Slide 9: MODIS (Moderate Resolution Imaging Spectroradiometer) AOD
http://terra.nasa.gov/About/
Orbit: | 705 km, 10:30 a.m. descending node (Terra) or 1:30 p.m. ascending node (Aqua)
Swath Dimensions: | 2330 km (cross track) by 10 km (along track at nadir)
Spatial Resolution: | 250 m (bands 1-2) 500 m (bands 3-7) 1000 m (bands 8-36)
Courtesy :NESDIS
National correlation map between AIRNow measurement and MODIS AOD
Typically good correlation between
surface PM2.5 and AOD retrieved
by MODIS
13th CMAS Oct27-29, 2014, Chapel Hill

## Slide 10: Optimal Interpolation (OI)
OI simplifies the extended Kalman filter formulation (Dee et al. Q. J. R. Meteor. Soc. 1998) by limiting the analysis problem to a subset of obs.
Obs far away (beyond background error correlation length scale) have no effect in the analysis.
Injection of Obs through OI takes place at 1800 UTC daily.
13th CMAS Oct27-29, 2014, Chapel Hill

## Slide 11
MODIS AOD & AIRNow PM2.5 assimilated
For initial condition adjustment
00Z
06Z
12Z
19Z
AIRNOW PM2.5, PM10, Ozone
MODIS AOD (Terra and Aqua)
14Z
17Z
18Z
13th CMAS Oct27-29, 2014, Chapel Hill
Tang (Poster Mon35)
Notes: 6 hour forecasts and retain the optimal analysis states

## Slide 12: Analysis field Verification: AIRNOW O3 & PM 2.5 over CONUS
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.

## Slide 13: Analysis field Verification: AIRNOW O3 & PM 2.5 over NE

## Slide 14
WRF 3.2.1 for meteorological fields
  NCEP North American Regional Reanalysis (NARR) 32-km resolution inputs
  NCEP ADP surface and soundings observational data
  MODIS landuse data for most recent land cover status
  3-D and surface nudging, Noah land-surface model
SMOKE 2.6 for CMAQ ready gridded emissions
  NEI inventory projected to 2011 using EGAS growth and existing control strategies
  BEIS3 biogenic emissions based on BELD3 database
  GOES biomass burning emissions: ftp://satepsanone.nesdis.noaa.gov/EPA/GBBEP/
CMAQ 4.6 revised to simulate gaseous & PM species
  SAPRC99 mechanism, AERO4, ISORROPIA thermodynamic, Mass conservation,
  Updated SOA module (Baek et. al. JGR 2011) for multi-generational oxidation of semi-volatile organic carbons
Analysis fields as IC and forecast with Total AOD Assimilation basis for LBCs
12 km
36 km
4 km
IC/BC of Base and AOD_DA cases
DISCOVER-AQ
GA_Tech
4 km
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Calculate differences between forecasts (B) and observations (O) at each AIRNOW station as a time series
Pair up AIRNOW stations, and calculate the correlation coefficients between the two time series at the paired stations
Plot the correlation as a function of the distance between the two stations,
Intercept Rz can be used to calculate the ratio between model error (EB) and and observational error (including representative error)
Horizontal length scale can be inferred as well

## Slide 15: Analysis field Verification: AIRNOW O3 & PM 2.5 over BW SIP
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.

## Slide 16
PM2.5 24h avg | Obs mean | Mean bias | RMSE | Corr. Coef.
L42 | 12.3 | -7.7 | 10.4 | 0.4
L42RAQMS | 12.3 | -5.4 | 8.5 | 0.5
L42-Fire1 | 12.3 | -7.6 | 10.6 | 0.3
L42-Fire1-OI4 | 12.3 | -1.11 | 6.65 | 0.61
CONUS
PM2.5 24h avg | Obs mean | Mean bias | RMSE | Corr. Coef.
Base | 19.8 | -0.67 | 24.18 | 0.49
With L42-Fire1-OI4 field to derive LBC | 19.8 | 1.15 | 5.79 | 0.53
DISCOVER-AQ
GA_Tech
4 km
Application of analysis field for State Implementation Planning
13th CMAS Oct27-29, 2014, Chapel Hill

## Slide 17
Configured forward-model vertical structure matching that of GFS
The reanalysis forward model is tested and used to generate July 2011
analysis fields for MDE for SIP modeling
Data Set assimilated: RAQMS (MLS, OMI O3, MODIS AOD); HMS Fire; GOES cloud fraction for photolytic rate correction; MODIS AOD; AIRNow O3, PM2.5
July 2011 analysis fields was compared to NAQFC simulation results
Next sets: lightning NOx; OMI SO2; PAR adjustment by retrievals
Verification to include data from O3 lidar network
Begin transition of assimilation algorithm to GSI
Production mode generation of analysis field for 2010
Summary
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: An important source of pm -- strong sensitivity to seasonality and geographical characteristics

## Slide 18
18
EXTRA SLIDES
Contact: Pius.Lee@noaa.gov
http://www.arl.noaa.gov/
13th CMAS Oct27-29, 2014, Chapel Hill

## Slide 19
Push towards higher resolution at NCEP
product | Targeted next | date | Remark
GFS | T878L64 ~ 22km | April 2014 | 
GDAS | T574 Enkr/GSI ~ 27 km | April 2014 | 
GEFS | T382L64 ~ 35 km | April 2014 | ~30 members
NAM | 12 km North America | Already in place | 
NAM | 3 km CONUS nest | July 2014 | 
NAM | On demand basis 1.3 km limited domain | Already in place | Fire weather
13th CMAS Oct27-29, 2014, Chapel Hill
Notes: Epidemiologists want at least hourly chemical composition of the lower atmosphere in 12 km resolution or finer.
NCEP’s push for finer horizontal grid spacing is a desirable trend.
This may mean a similar push for chemical reanalysis fields.

## Slide 20
Thank you for voicing support to NAQFC
“I am writing to comment on the
Proposed Termination of NWS Ozone Air Quality Predictions …
The NAQFC is the only numerical forecast model that is available every day,
is fully documented, accessible for evaluation, and shows good forecast skill.
It should be retained”. (November 1 2012, Bill Ryan, PSU)
On “The proposal to shelve the $5.4 million National Air Quality Forecasting
Capability in March has drawn protests from public health officials…”
(January 26 2013, Dan Vergano, USA Today)
November 2012,
MDE as Oppose_1
13th CMAS Oct27-29, 2014, Chapel Hill