## Slide 1
1
Simulating the phase partitioning of HNO3, NH3, and HCl with size-resolved particles over northern Colorado in winter
James T. Kelly1, Kirk R. Baker1, Christopher G. Nolte2, Sergey L. Napelenok2, William C. Keene3, and Alexander A. P. Pszenny4
1Office of Air Quality Planning & Standards, U.S. EPA, Research Triangle Park, NC
2Office of Research and Development, U.S. EPA, Research Triangle Park, NC
3Department of Environmental Sciences, University of Virginia, Charlottesville, Virginia
4Institute for the Study of Earth, Oceans and Space, University of New Hampshire, Durham, NH
Image provided by the NOAA/OAR/ESRL PSD, Boulder, CO, USA, from their website at http://www.esrl.noaa.gov/psd/
Acknowledgments: Daniel Wolfe, Bruce Bartram, William Dubé, Nicholas Wagner, U.S. EPA Modeling Platform Development Team, Allan Beidler, James Beidler, Chris Allen, Lara Reynolds, and Dr. Daniel Bon

## Slide 2
Motivation
Particle Diameter
Gas/particle equilibrium
Dynamic gas/particle mass transfer
Aitken
Accumulation
Coarse
NH3, HNO3, HCl
SO42-,
Mg2+, K+, Ca2+, Na+,
NH4+, NO3-, Cl-,
H2O
H2SO4
Temperature
RH
CMAQ’s inorganic PM predictions involve the partitioning of species between the gas phase and size-distributed particles
Comprehensive evaluations of these predictions are usually not possible due to incomplete observational datasets

## Slide 3
3
NACHTT Campaign
In Feb-Mar 2011, comprehensive observations of inorganic PM and trace gases were made in CO
Observations include
  Gas: NH3, HNO3, and HCl
  Size-segregated PM: SO42-, NH4+, NO3-, Cl-, Mg2+, Ca2+, and K+
  Meteorology: T, RH, wind speed and wind direction
Full suite of measurements to comprehensively evaluate inorganic aerosol predictions
NACHTT: Nitrogen, Aerosol Composition, and Halogens on a Tall Tower
*Image provided by the NOAA/OAR/ESRL PSD, Boulder, CO, USA, from their website at http://www.esrl.noaa.gov/psd/
BAO Tower
NOAA Boulder Atmospheric Observatory tower in Weld County, CO (40.0500°N, 105.0039°W)*

## Slide 4
4
Objectives
Primary objective
  Comprehensively evaluate CMAQ’s inorganic aerosol predictions for a site influenced by complex meteorology and emissions
Secondary objective
  Characterize contributions of emission sectors to predictions to the site using the CMAQ-ISAM* source apportionment model
*ISAM: Integrated Source Apportionment Model

## Slide 5
5
Modeling
Air quality modeling
  CMAQv5.0.2
  12 km horizontal resolution
  25 vertical layers
  CB05tucl gas-phase chemistry
  AERO6 aerosol processes
Emissions
  NEI11 version 2
  BEISv3.6.1 biogenic emissions
  NH3 bidirectional surface exchange
Meteorology
  WRF version 3.4, MCIP 4.1.3
Boundary conditions
  GEOS-Chem version 8-03-02
  2° x 2.5° horizontal resolution
Air Quality Modeling Domain w/ BAO Tower
Simulations discussed below
  Base: configuration shown on left
  x4nh3: NH3 emissions scaled by four
  ISAM: CMAQ with Integrated Source Apportionment
  B-F: brute-force runs using “Base”

## Slide 6
6
Site Location
~33 km
Denver
Greeley
BAO Tower
  ~33 km north of Denver
  Southwest of numerous animal feedlots
  East of Front Range
  Sampling from 22-m agl
NH3 emissions
  Elevated in region with animal feedlots and Denver (see figure)
Challenging conditions
  Diverse emission sources and complex terrain
RMNP
Colors indicate average NH3 emissions in model cells
BAO: Boulder Atmospheric Observatory
RMNP: Rocky Mountain National Park

## Slide 7
Inorganic Trace Gases
NH3 observations are underpredicted in Base simulation but predicted reasonably well in x4nh3 simulation
HNO3 observations are underpredicted in both simulations, more severely in x4nh3
HCl observations are substantially underpredicted in both simulations

## Slide 8
Inorganic PM Components
NH4+ is underpredicted in both cases; NH4+ predictions for x4nh3 are improved compared with Base but are closer to Base than to measurements
Little difference in SO42- predictions for the Base and x4nh3 cases (as expected); both simulations underpredict infrequent high SO42- measurements
NO3- is underpredicted in Base case; NO3- predications are improved in x4nh3 case
Cl- and Na+ are underpredicted; Ca2+, Mg2+, and K+ are overpredicted

## Slide 9
PM Size Distributions
Distributions of NO3- (and NH4+ and SO42-) agree reasonably with observations but are shifted to slightly larger diameters
Na+ distributions are predicted well but coarse Na+ is underpredicted; coarse Cl- is underpredicted
Ca2+ (and Mg2+ and K+) is overpredicted in all size fractions
Note: outlier points not shown in figure for clarity

## Slide 10
Total Levels (Gas + Particle)
Large underestimate of observed total ammonium (NH3+NH4+) in Base; better agreement in x4nh3
Observed total nitrate (HNO3+NO3-) is moderately underestimated in Base; slightly better agreement for x4nh3
Large underestimate of observed total chloride (HCl+Cl-) in Base; slightly better agreement for x4nh3

## Slide 11
Gas Fraction (Gas / Total)
Total ammonium partitions mostly to the gas phase in all cases; close agreement between observations and x4nh3 estimates
Total nitrate partitions too much to the gas phase in Base and too much to the particle phase in x4nh3
Total chloride partitions too much to the gas phase in Base; close agreement between observations and x4nh3 estimates

## Slide 12
Source Apportionment
Agricultural sector is largest contributor to NHx
Mobile sources are largest contributors to HNO3 & NO3-
EGUs are largest contributors to SOx
Area fugitive dust is largest contributor to fine particle Ca2+
RWC is largest contributor to fine particle K+
Boundaries are largest contributors to fine Na+ and Cl-

## Slide 13
Contributions of RWC to K+
Good agreement in spatial patterns and magnitude of residential wood combustion contributions to fine-mode K+
Percent contribution of RWC to fine mode K+ at the BAO site is 34% for CMAQ-ISAM and 33% for brute-force

## Slide 14
Boundary Contribution to NO3-
General agreement in spatial patterns of the contribution of boundary NOy to fine-mode NO3- concentrations
Percent contribution of boundary NOy to total NO3- at the BAO site is 14% for CMAQ-ISAM and 7% for brute-force

## Slide 15
Summary
CMAQ predictions capture the general features of observed distributions of gas mixing ratios, size-distributed particle concentrations, and gas-particle partitioning fractions
CMAQ-ISAM source apportionment estimates are consistent with expectations based on major emission sectors and provide useful insights in some cases
Areas for improvement have been identified
  NH3 emissions, presumably from nearby animal feedlots, to help address NHx underpredictions, which appear to be related to emissions and transport
  Flux and speciation of fugitive and windblown dust emissions to help address mineral cation overpredictions and chloride underpredictions
  NOy boundary conditions in Alberta, Canada region
  Additional testing of CMAQ-ISAM and comparison with other source apportionment methods is warranted for secondary PM
  Better representation of terrain-influenced winds with finer-scale modeling to improve temporal characteristics of predictions

## Slide 16
Additional Slides

## Slide 17
Conceptual Meteorology
Evening
Day
Denver
Downslope Events
S. Platte River
Meteorology is influenced by terrain
  Daytime upslope flows in Rocky foothills
  Nocturnal drainage flows along South Platte River valley
  Downslope wind events associated with synoptic forcing

## Slide 18
18
Meteorology
(a)
(b)
Generally light and variable winds captured by model (Fig. a)
High speed westerlies captured by the model; model does not replicate high speed northeasterlies (Fig. a)
Modeled winds too frequent from west; too infrequent from northeast (Fig. b)