## Slide 1: Enhancements to an Agricultural Land Modeling System – FEST-C and Its Application
Ellen Cooter1, Limei Ran1, Verel Benson2, Dongmei Yang3,
Jesse Bash1, Ruoyu Wang1, and Yongping Yuan1
1ORD NERL/USEPA, Research Triangle Park, NC
2Verel W. Benson, Benson Consulting
200 Haywood Ct, Columbia, MO 65203, USA
3Institute for the Environment
University of North Carolina at Chapel Hill, NC USA

## Slide 2: Presentation Outline
FEST-C Description
Software download, installation and execution
FEST-C V1.2 Enhancements and Updates
Recent Applications
Future Enhancements

## Slide 3: Fertilizer Emission Scenario Tool for CMAQ (FEST-C)
Produces initial soil nitrogen pool and fertilizer activity inputs required to run bi-directional CMAQ
FEST-C v1.0: first release in 10/2013
FEST-C v1.2: current release 05/2016
Any CMAQ or GEOS-CHEM CONUS domain (e.g., 12km US1, DISCOVER-AQ 4km)
Other regions (e.g. China) with adapted land use, crop, soil and other data
Soil & Water Assessment Tool

## Slide 4
Where do I get FEST-C?
  CMAS (includes installation instructions, users manual and tutorial
What do I need to install FEST-C (US1 12km domain)?
  Linux (5G to install, 4G memory, output needs 14 GB/yr )
  SA (required) and VERDI (optional)
  Installed and tested on UNC (KittyHawk), NCC (SOL), HPCC and Dell T7600 (CAUTION: many small files)
How do I run FEST-C?
  Interface-driven (FEST-C)
  Background execution (time varies with host configuration)
  Software creates and executes scripts

## Slide 5
What input data do I need?
  Simulation cell size, domain extent and projection
  MCIP formatted weather data on same domain as you will run CMAQ (currently need full year)
  MODIS and NLCD data layers
What data are provided/generated
  BELD coverage (location of agricultural land)
  Soils
  Agricultural management
  All other input files needed to simulate biogeochemistry
What do I get out?
  BELD file required for bidirectional CMAQ (tool provided with SA)
  Daily agricultural depth of fertilizer application and fertilizer amount
  Initial soil chemistry status
  Other N pool information that can be used to support further CMAQ model development, e.g., new NO model.

## Slide 6: FESTC V1.2 System : Enhancement and Updates
  Addition of tile drain management option for crops
  Improved evapotranspiration parameterization
  Improved pasture and wheat management
  User-defined ambient CO2 concentration
  Elevation input update
  Average N deposition input options (2002-2006, 2006 – 2010)
  R post-processing tool kit
Environmental Policy Integrated Climate model
FEST-C interface

## Slide 7
  Support to the 2014 NEI
  China air quality simulations
  Exploring land use and emissions changes
  One-Biosphere integration
FESTC V1.2: Applications

## Slide 8
Contributions to 2014 NEI
FEST-C results provide “fertilizer activity” data and drive bidirectional CMAQ estimates of agricultural soil NH3 emissions for the 2014 NEI. They offer an alternative to previous Carnegie-Mellon University model estimates.

## Slide 9
 | bidi | nobidi
NMB | 5.0% | 21.4%
NME | 34.9% | 57.3%
Bidirectional CMAQ/FEST-C for China
Bidirectional CMAQ/FEST-C ambient NH3 estimates show better general agreement with observations, particularly during high-concentration periods in November.
(Fu et al., 2015) http://www.atmos-chem-phys.net/15/6637/2015

## Slide 10
Exploring Multimedia Consequences
of Land Use Change
Bidirectional CMAQ can simulate Nr emission (and deposition) response to FEST-C estimates of N fertilizer application and land use or land management changes.
Projected Grain Corn Increases
Soil NH3 Emission Response

## Slide 11: Linking Air, Land and Water
  SWAT is a USDA water quality model. EPA Office of Water uses its HAWQS interface to run SWAT. This figure compares monthly streamflow and NO3 from HAWQS and SWAT-EPIC to USGS 07373420 obs near St. Francisville, LA.
CMAQ and FEST-C are part of a One-Biosphere modeling system that explores hypoxia in the northern Gulf of Mexico associated with N loads from the Mississippi River and atmospheric deposition. Here we compare nitrate loads without (HAWQS) and with CMAQ and FEST-C (EPIC) inputs.

## Slide 12: Future Enhancements
New release with improved N (N2O emissions), Carbon and soil water algorithms and modular code design (FY17)
Eliminate need for full year of MCIP input (FY17)
Wind erosion (FY17)
Additional output variables to support One Biosphere modeling e.g., Harmful Algal Blooms (HAB’s) and Northern Gulf of Mexico hypoxia prediction (FY17)
LAI estimates for natural mix forest stands (bidi implementation in FY18)
Full implementation of vegetation and hydrologic cycle (ET) response to increasing CO2 (run with dynamically downscaled WRF-Climate inputs) (FY18)