## Slide 1
Title
Carolina First Steering Committee
October 9, 2010
Equatorward redistribution of emissions dominates the 1980 to 2010 tropospheric ozone change
Yuqiang Zhang1,2, Owen R, Cooper3,4, Audrey Gaudel3,4, Anne M. Thompson5, Philippe Nedelec6, Shin-Ya Ogino7, J. Jason West1
1 Environmental Sciences and Engineering, University of North Carolina at Chapel Hill
2 now at US Environmental Protection Agency
3 Cooperative Institute for Research in Environmental Sciences, University of Colorado
4 Chemical Sciences Division, NOAA Earth System Research Laboratory
5 NASA Goddard Space Flight Center
6 CNRS Universite Paul Sabatier Toulouse
7 Japan Agency for Marine-Earth Science and Technology
Paper in press with Nature Geoscience

## Slide 2
Global ozone precursors shifting southwards
Anthropogenic NOx emissions (including biomass burning) from ACCMIP and RCP8.5.
1950
1960
1970
1980
1990
2000
2010
Notes: Ozone precursors are increasing globally from 1980 to 2010.
CO & NMVOCs increases at south of 30˚N, but decreases north of this latitude from 1980 to 2010.
NOx increase south of 40˚N, but decreases north.
The peak emission regions shifts southwards.

## Slide 3
Global tropospheric O3 burden much more sensitive to emissions from the tropics and SH
Sensitivity of global trop. O3 burden to changes in NOx emissions, based on simulations of 10% NOx reductions from 9 world regions (West et al., 2009).

## Slide 4
Global Anthropogenic Emission Changes, 1980-2010
Anthropogenic emissions (including biomass burning) from ACCMIP and RCP8.5.
Global CH4 mixing ratio +15%
 | Global | Tropics (23°S-23°N)
NOx | +21% | +49%
CO | +6% | +22%
NMVOCs | +6% | +16%

## Slide 5
Objectives
Separate the changes in the global tropospheric ozone burden (BO3) from 1980 to 2010 into contributions from changes in:
  the spatial distribution of anthropogenic short-lived pollutant emissions,
  the global magnitude of these emissions, and
  the global CH4 mixing ratio.

## Slide 6
Global CTM: CAM-chem (Lamarque, 2012)
Anthropogenic and biomass burning emissions are from ACCMIP for 1980 and RCP8.5 for 2010 (Lamarque, 2010; Riahi, 2011).
Biogenic emissions are calculated on-line using MEGAN-v2.1 (Guenther, 2012)
Global meteorology is from NASA GEOS-5 for 2008-2012.
 | Emission total in year | Spatial pattern in year | CH4 concentration
S_2010 | 2010 | 2010 | 1798 ppb
S_1980 | 1980 | 1980 | 1567 ppb
S_Distribution | 2010 | 1980 | 1798 ppb
S_Magnitude | 1980 | 2010 | 1798 ppb
S_CH4 | 2010 | 2010 | 1567 ppb
Simulations carried out for this study
Methods
Notes: All the models are run for consecutive five years and we use four years average for the data analysis. We apply the same meteorology for all the simulations, neglecting the effects of climate change or variability.
Explain the three sensitivity scenarios.

## Slide 7
Tropospheric O3 burden change, 1980 to 2010
The change in the emission spatial distribution contributes slightly more to the total BO3 change than the emission magnitude and methane changes combined.
Methane
Distribution
Magnitude
Total
Notes: 1. Global BO3 have increased by 28.12 Tg from 1980 to 2010, with NH accounting for 57%.
2. slightly greater than the combined influence of the change in emission magnitude (8.59 Tg) and the global CH4 change (7.48 Tg)

## Slide 8
Tropospheric O3 burden change, 1980 to 2010
Greatest BO3 increases are over South and Southeast Asia.

## Slide 9
Tropospheric O3 burden change, 1980 to 2010
The change in spatial distribution of emissions best explains the magnitude and pattern of the overall change.
Total
Spatial distribution
Methane
Magnitude

## Slide 10
O3 increases most over 0°N-35°N from the surface to the upper troposphere, and over 30°S-0°S
The spatial distribution change best explains the overall change.
Total
Spatial
distribution
Magnitude
Global CH4
Zonal distributions of tropospheric O3 changes
Latitude Latitude

## Slide 11
Total
Spatial
distribution
Magnitude
Global CH4
Zonal distributions of tropospheric NOy changes
Latitude Latitude
Emission increases <35ºN are transported efficiently upward, due to strong Hadley cell convection.
Emission decreases >35ºN stay at higher latitudes and lower elevation.

## Slide 12
OMI/MLS
Modeled 2010
Model - OMI/MLS

## Slide 13
11-year OMI/MLS satellite O3 column trends (2004-2015), white circles show statistically significant positive trends.
Modeled O3 burden change (1980 to 2010)

## Slide 14
IAGOS commercial aircraft O3 profiles to/from several airports (incl. Hong Kong, Bangkok, Hanoi, Ho Chi Minh City, Guangzhou), SHADOZ ozonesondes over Hanoi.
First observed significant O3 increase over SE Asia.
SE Asia ozone profiles

## Slide 15
Change in NOx emissions (1980-2010)
Sensitivity of O3 burden to NOx emissions (West et al. 2009)
Change in O3 burden due to regional emission changes

## Slide 16
Conclusions
Changes in the spatial distribution of global anthropogenic emissions dominate the 1980-2010 tropospheric O3 burden change, slightly larger than the combined effect of the global emission magnitude and global CH4 change.
O3 production is much more sensitive to emissions from tropical and subtropical regions due to strong photochemical rates, NOx-sensitivity, and strong convection, despite a shorter O3 lifetime.
Emissions increases from South and Southeast Asia may be particularly important for the global BO3 increase.
The future ozone burden will be determined mainly by emissions from the tropics and subtropics.
A continued equatorward shift may cause BO3 to increase, even if global emissions decrease.
Y. Zhang et al., Nature Geoscience, in press

## Slide 17: Thank you
Thanks for help, data, and analysis tools from: Jerry Ziemke, Louisa Emmons, Simone Tilmes, Jim Schwab, and Paul Young.
Funding Sources:
EPA STAR Grant #834285
NIEHS Grant #1 R21 ES022600-01
834285
UNC Climate Health and Air Quality Lab
www.unc.edu/~jjwest
Notes: 17

## Slide 18
Model evaluation
Chart: Barrow
| 1980 | 2010
Model | 30.158 | 31.9551
Obs | 26.4083 | 26.9958
Chart: Hohenpeissenberg
| 1980 | 2010
Model | 43.6643 | 50.4315
Obs | 34.6582 | 40.5772
Chart: Whiteface Mountain
| 1980 | 2010
Model | 49.5023 | 48.5053
Obs | 38.618 | 36.9189
Chart: Manua Loa
| 1980 | 2010
Model | 43.2863 | 49.1451
Obs | 38.6646 | 42.0542
Chart: Samoa
| 1980 | 2010
Model | 11.9022 | 13.4019
Obs | 13.6375 | 13.5833
Chart: South Pole
| 1980 | 2010
Model | 19.6344 | 20.9733
Obs | 29.1333 | 29.4792
The model reproduces the O3 trend from 1980 to 2010 at six long-term remote sites well.
The model also performs well for O3 seasonal, spatial, and vertical distribution in 2010.
Notes: 1. We compare the O3 trend from 1980 to 2010 at six long-term remotes sites between model outputs and observations, and found that the model reproduces the trend well.
2. By comparing model output with multi-year ozonesonde data, satellite data, aircraft campaigns, and ground-based observation data, though with a tendency to overestimate surface O3

## Slide 19
ΔBO3 at different latitudinal bands
∆BO3 from 1980 to 2010 are greatest over the tropical regions, from 30ºS to 30ºN (17.93 Tg).
For different latitudinal bands, the effect of the change in emission spatial distribution changes is always larger than that from emission magnitude and global CH4, except for north of 60ºN.
Notes: Then we take a look at the global O3 burden changes at different latitudinal bands.

## Slide 20
Strong NOx-sensitivity is prevalent over tropical regions, especially in the middle and upper troposphere (not shown here), and emission trends show greater increases of NOx than of VOCs.
O3-NOx-VOCs sensitivity
VOC-sensitive← → NOx-sensitive VOC-sensitive← →NOx-sensitive
H2O2/HNO3 ratio
H2O2/NO2 ratio
Annual average surface ratios

## Slide 21
Tropical regions have fast chemical reaction rates due to strong sunlight and high temperature.
Global O3 chemical production and loss rate

## Slide 22
IAGOS commercial aircraft O3 profiles to/from several airports (incl. Hong Kong, Bangkok, Hanoi, Ho Chi Minh City, Guangzhou), SHADOZ ozonesondes over Hanoi.
First observed significant O3 increase over SE Asia.

## Slide 23
IAGOS commercial aircraft O3 profiles over northeastern China to/from several airports.
Extends observations of positive trend by Ding et al. (2008).

## Slide 24
IAGOS commercial aircraft O3 profiles over southern India to/from several airports.