## Slide 1: Potential Performance differences of the National Air Quality Forecasting Capability when upgrading the Chemical Transport Model
Pius Lee1, Youhua Tang1,2, Jeff McQueen3, Ivanka Stajner3,4, Daniel Tong1,2,5,
Barry Baker1,2, Hyuncheol Kim1,2, Jianping Huang3,6, Ho-Chun Huang4,6,
Li Pan3,6, and Jose Tirado-Delgado7
1NOAA Air Resources Laboratory; 2 UMD Cooperative Institute for Climate and Satellites, 3 NOAA National Centers for Environmental Prediction (NCEP); 4 NOAA NWS Office for Science and Technology Integration; 5 Center for Spatial Information Science and Systems, George Mason University; 6 I.M. Systems Group Inc., Rockville; 7Eastern Research Group (ERG), Arlington,
17th CMAS, Oct 22-24 2018

## Slide 2
Current NAQFC & CMAQ5.2 strengths in NAQFC-γ;
Long range transport of Smoke and Dust plumes;
Time-varying LBCs in NAQFC using GEOS-Chem & NGAC input;
Time-varying LBCs in NAQFC-γ using hemispheric CMAQ input;
Investigated to include halogen chemistry (reduction in coastal O3).
Talk Outline
17th CMAS, Oct 22-24 2018

## Slide 3
CMAQ5.0.2 (155 species) : major improvement since last upgrade
  Explicitly modeling NTR by various alkyl nitrates species
  Improved dust and PM modeling by adding 17 mineral species
Current Operations over CONUS
Exploring CMAQ5.2 with developmental runs:
  SOA module with enhanced summer time production of SOA;
  CB6 and aero6 – 228 species: Advancement VOC chemistry & Combustion PM;
  Photolysis rate attenuation from aerosol diming;
  Account gas-chemistry by adopting EPA smoke-2-cmaq chemical profile;
  LBC from operational NGAC for intruding smoke plume species;
  Dynamic boundary condition from hemispheric CMAQ simulation;
  Halogen chemistry: Cl, Br, and I.
17th CMAS, Oct 22-24 2018

## Slide 4
A typical monthly hot-spot fire count in April
Account for Exo-domain emitted pollution intruded into CONUS via BCs
Dust storm plume transported from West Africa
Courtesy: LANCE Rapid response team,
NASA
17th CMAS, Oct 22-24 2018

## Slide 5
Static LBC
Monthly averaged vertical profiles from GEOS-CHEM 2006
(a) ASOIL
(b) ASO4J
Current ops: PM components are modified by NGAC
17th CMAS, Oct 22-24 2018

## Slide 6
Seasonality of chemical lateral boundary conditions
(a) Geos5 2015 January monthly averaged CO
(b) Geos5 2015 April monthly averaged CO
17th CMAS, Oct 22-24 2018

## Slide 7
Modify static Chemical LBC with NGAC 3-hourly output
Dynamic BC data are fed into CMAQ
NGAC species | CMAQ species (multiplicative factor) | 
Dust | A25J | 1.0, 0.42; respectively (R.)
Dust | ASOIL | 0.58,1.0,0.76; (R.)
Sea salt | ANAJ | 0.39,0.27; (R.)
Sea salt | ACLJ | 0.61,0.42(R.)
Sea salt | ANAK | 0.12,0.39; (R.)
Sea salt | ACLK | 0.18,0.61; (R.)
SO2 | SO2 | 1.0
CO | CO | 1.0
SO4 | ASO4J | 1.0
bcphobic | AECJ | 1.0
bcphilic | AECJ | 1.0
ocphobic | AORGPAJ | 1.0
ocphilic | AORGPAJ | 1.0
Speciation mapping between NGAC and CMAQ speices
17th CMAS, Oct 22-24 2018

## Slide 8
17th CMAS, Oct 22-24 2018
Case | CTM | Dynamic LBC | Halogen emission | Remark
V5.2_Base | CMAQ5.2 | NGAC no gaseous species | none | 17 species
V5.2_LBC_A | CMAQ5.2 | Derived from hemispheric CMAQ | none | 230 species
V5.2_LBC_B | CMAQ5.2 | Derived from hemispheric CMAQ | Parameterized based on chlorophyll-a concentration | 230 species
Sensitivity cases for exploring CMAQ5.2 to include Halogens
Courtesy : Sarwar Golam

## Slide 9
Unraveled LBC along perimeter of CMAQ-CONUS domain
(a) Static from climatology
(b) Overridden by NGAC
CMAQ species can be strongly modified by corresponding species in NGAC
17th CMAS, Oct 22-24 2018
Notes: (Q) What & specificity, result of pre-implementation test Phase I

## Slide 10
Polar stereographic projection
with 44 layer & model top at 50 mb
Courtesy : Sarwar Golam
17th CMAS, Oct 22-24 2018
Derive dynamic LBC from Hemispheric CMAQ5.2 simulation
Lambert Conformal Conic projection with 35 layer & model top at 50 mb

## Slide 11
17th CMAS, Oct 22-24 2018
Surface O3 valid 20180705 17Z
V5.2_LBC_A -- LBC hemispheric CMAQ but
no CHLO based Cl,Br, I emission
V5.2_LBC_B minus V5.2_LBC_A
V5.2_Base -- LBC no gaseous species

## Slide 12
17th CMAS, Oct 22-24 2018
V5.2_LBC_B minus V5.2_LBC_A
Surface O3 valid 20180705 17Z
V5.2_LBC_B -- LBC hemispheric CMAQ and
with CHLO based Cl,Br, I emission
V5.2_LBC_A -- LBC hemispheric CMAQ but
no CHLO based Cl,Br, I emission

## Slide 13
17th CMAS, Oct 22-24 2018
O3
PM2.5
Variability for V5.2_LBC_B and
V5.2_LBC_A cases are comparable and better than current NAQFC.

## Slide 14
17th CMAS, Oct 22-24 2018
 |  | N | obs | mean | Bias | RMSE | Coeff corr | FAR | IOA
 | 5.2 NGAC | 271300 | 33.0 | 38.25 | 5.25 | 12.94 | 0.71 | 0.72 | 0.82
 | N_CHLO |  |  | 38.87 | 5.87 | 12.98 | 0.73 | 0.71 | 0.82
 | CHLO |  |  | 38.42 | 5.42 | 12.83 | 0.73 | 0.71 | 0.83
NE | 5.2 NGAC | 39500 | 34.8 | 39.20 | 4.40 | 13.05 | 0.75 | 0.64 | 0.85
 | N_CHLO |  |  | 40.15 | 5.35 | 13.04 | 0.77 | 0.62 | 0.85
 | CHLO |  |  | 39.78 | 4.98 | 12.94 | 0.77 | 0.62 | 0.86
S E | 5.2 NGAC | 45300 | 26.0 | 34.28 | 8.28 | 13.84 | 0.67 | 0.92 | 0.73
 | N_CHLO |  |  | 34.82 | 8.82 | 13.85 | 0.69 | 0.92 | 0.75
 | CHLO |  |  | 34.53 | 8.53 | 13.71 | 0.69 | 0.92 | 0.76
SC | 5.2 NGAC | 39000 | 35.8 | 39.96 | 4.16 | 14.03 | 0.71 | 0.65 | 0.65
 | N_CHLO |  |  | 40.56 | 4.76 | 14.66 | 0.70 | 0.65 | 0.65
 | CHLO |  |  | 39.67 | 3.87 | 14.42 | 0.70 | 0.65 | 0.65
CONUS
MDA8 O3 performance for CMAQ5.2 configurations in 7/1-7/11

## Slide 15
17th CMAS, Oct 22-24 2018
 |  | N | obs | mean | Bias | RMSE | Coeff corr | FAR | IOA
 | 5.2 NGAC | 183530 | 8.9 | 9.20 | 0.30 | 11.13 | 0.23 | 1.0 | 0.44
 | N_CHLO |  |  | 9.32 | 0.42 | 11.55 | 0.22 | 1.0 | 0.42
 | CHLO |  |  | 9.32 | 0.42 | 11.55 | 0.22 | 1.0 | 0.42
NE | 5.2 NGAC | 25300 | 10.0 | 11.58 | 1.58 | 8.68 | 0.46 | 1.0 | 0.66
 | N_CHLO |  |  | 11.86 | 1.86 | 8.89 | 0.44 | 1.0 | 0.65
 | CHLO |  |  | 11.85 | 1.85 | 8.89 | 0.44 | 1.0 | 0.65
S E | 5.2 NGAC | 23500 | 8.6 | 9.26 | 0.66 | 7.90 | 0.20 | 1.0 | 0.45
 | N_CHLO |  |  | 9.36 | 0.76 | 8.47 | 0.18 | 1.0 | 0.42
 | CHLO |  |  | 9.36 | 0.76 | 8.47 | 0.18 | 1.0 | 0.42
SC | 5.2 NGAC | 43800 | 7.9 | 6.53 | -1.37 | 9.32 | 0.31 | 0.99 | 0.47
 | N_CHLO |  |  | 6.72 | -1.18 | 9.24 | 0.30 | 0.99 | 0.47
 | CHLO |  |  | 6.71 | -1.19 | 9.24 | 0.31 | 0.99 | 0.47
CONUS
24 h PM2.5 performance for CMAQ5.2 configurations in 7/1-7/11

## Slide 16
Current NAQFC & CMAQ5.2 strengths in NAQFC-γ
Long range transport of Smoke and Dust plumes;
Time-varying LBCs in NAQFC using GOES-Chem & NGAC input;
Time-varying LBCs in NAQFC-γ using hemispheric CMAQ input;
Investigated to include halogen chemistry (reduction in coastal O3?)
Improved variability characteristics of surface O3 and PM2.5;
Reduced over-predictions in coastal O3.
Tested CMAQ5.2 configurations for NAQFC-γ
17th CMAS, Oct 22-24 2018
Other NAQFC presentations: Mon_3.10: Kim et al. NO2 down-scaling
PI (18) Tang et al., Hawaii volcano eruption; Wed_1.00: Tong et al., Dust emission
PI (23) Baker et al., Evaluation Toolkit (MONET); Wed_4.10: Stajner et al., NAQFC
PII (5) Kim et al., Top-down NO2; : Chai et al., Smoke inverse modeling