## Slide 1
Authors
Ankur Prabhat Sati & Gerald Mills
School of Geography, University College of Dublin Ireland
Multi-scale modeling of urban carbon emissions: Integrating WRF and MUNICH models in Dublin, Ireland
22nd Annual CMAS Conference 2023
World Urban Database and Access Portal Tool (WUDAPT),
special session in honor of Jason Ching

## Slide 2
The main objective of the present work is the estimation of urban greenhouse emissions using WRF-chem over Ireland with a final focus on the capital city, Dublin using MUNICH model
WRF-chem Model set-up
Local Climate Zones (LCZs) in WRF Model
Vegetation Photosynthesis and Respiration Model (VPRM)
Model performance evaluation
Model of Urban Network of Intersecting Canyons and Highways (MUNICH)
Conclusions
Contents

## Slide 3
Ireland has an objective of climate neutrality by 2050 with an interim target of a 51% reduction in GHG emissions by 2030 relative to a baseline of 2018.
Ireland and Greenhouse gas emissions
 | Ireland | N Carolina | US
Area (sq km) | 70,273 | 139,390 | 9,833,520
Population (million) | 5.1 | 10.6 | 331
Largest city Pop (Million) | Dublin 1.26 | Charlotte 1.38 | New York 19.4
Public Services 1.1
Waste 1.4
Energy Industries 16.6
Residential 10.0
Industrial Process 3.8
F-gases 1.2
Transport 19.1
Agriculture 38.4
Commercial services 1.3
Manufacturing Combustion 7.1
% share in GHG emissions 2022, https://www.epa.ie/

## Slide 4
Greenhouse gas studies in Ireland
Terrain AI: Understanding of GHG exchange across landscapes viz., farms, forests, peatlands, and urban spaces.
Multidisciplinary: AI and computational methodologies for the collection, modeling, and fusion of multi-thematic data
NEXSYS: Innovative solutions across different scales of the urban landscape including neighborhood scales, collectives of large municipal buildings, new and retrofit housing and data centres
https://terrainai.com/

## Slide 5
Emissions in Urban Areas
Various studies focus on anthropogenic emissions for urban areas. Mitigation policies include reducing emissions in various sectors eg., transport, energy (powerplants), residential uses etc
The Climate action plans of every city include greening of cities. We need a comprehensive framework to assess the combined impact of reducing anthropogenic emissions and greening towards becoming “Carbon-Neutral” cities.
A very few studies deal with CO2 sequestration by urban vegetation. An uptake of 1.4 ton km−2 day−1 was estimated for an urban neighborhood in Singapore (Velasco et al., 2013)
We intend to use modeling techniques to understand the role of vegetation, initially trees, on CO2 emissions in an urban landscape.

## Slide 6
The work involves updating various datasets for the model over the study region
Meteorology: ERA5 Reanalysis
Chemistry: Greenhouse gases Mode
Landuse - CORINE
Urban Form - LCZs
Biogenic Emissions -VPRM
Anthropogenic- EDGAR V6.0
WPS
geogrid
ungrib
metgrid
Domain Setup
Land Use
Meteorological data
Real Data
WRF chem
Model Output and Visualization
Biogenic Emissions
VPRM
Anthropogenic Emissions EDGAR
Boundary Conditions
CMAS Reanalysis
Convert_emiss
Chem
Model setup (WRF-LCZ-GHG)

## Slide 7
Simulation Period:
May 2020 (Summer Period)
Domain | Resolution (km) | Grids | Expanse (km2)
1- Outer | 10 | 252 × 345 | 8,694,000
2- Middle | 1 | 551 × 611 | 336,661
3- Inner | 0.25 | 137 × 81 | 694
Triple nested domain setup covering Ireland and Dublin city
(a) Ireland at 1km (b) Dublin city area
LCZs around Dublin show presence of LCZ 6 (Open low-rise), LCZ 4 (Open high-rise) and LCZ 2 (Compact midrise in the city center}.
A WUDAPT-to-WRF python tool that injects WUDAPT's Local Climate Zone information into WRF.
(Demuzere et al., 2021)

## Slide 8
WRF simulated meteorology at two stations around Dublin
Dublin Airport
Casement
RMSE units: Temp-K, wind speed-m/s, RH- %
Model: WRF+LCZ
Resolution: 250 m
Period: May 2020

## Slide 9
Anthropogenic emissions
EDGAR v6.0 provides emissions of the three main greenhouse gases (CO2, CH4, N2O) and fluorinated gases per sector and country.
CO2 emissions include all fossil CO2 sources, such as
fossil fuel combustion,
non-metallic mineral processes (e.g. cement production),
metal (ferrous and non-ferrous) production processes,
urea production,
agricultural liming and solvents use.
Large scale sources and sinks from Land-use, Land-use Changes and Forestry (LULUCF) are excluded.
Average emission rates for CO2 (kg m-2 s-1)

## Slide 10
Biogenic CO2 Fluxes - VPRM model
The parameters Tscale , Pscale and Wscale account for the temperature sensitivity of photosynthesis, effects of leaf age on canopy photosynthesis, and the effect of water stress on GEE
The VPRM preprocessor generates: Vegetation Fraction (VEGFRA), MODIS Land Surface Water Index (LSWI) and Enhanced Vegetation Index (EVI)
VEGFRA, EVI and LSWI for the major vegetation class ‘grasslands’ across inner domain.

## Slide 11
Pasture-based grass growth Ireland 2020-2023
WRF-chem simulated contribution of biogenic CO2 (ppm) for day and night-time.
WRF-Chem (VPRM) generated Biogenic CO2 emissions
The vegetation utilizes CO2 during daytime (around 3-4 ppm)
Slight increase in biogenic CO2 during night owing to respiration
Day
15 h
Night01 h
CO2
https://www.teagasc.ie/

## Slide 12
Model Performance Evaluation
Met Evaluation at Dublin
CO2 Evaluation
CH4 Evaluation
Improvement in meteorology after inclusion of LCZs
Model simulates the averaged and peak GHG values
The diurnal trend of meteorology and GHGs is captured
 | MBE |  | RMSE |  | r (unitless) | 
 | Slab | LCZ | Slab | LCZ | Slab | LCZ
Temperature (K) | -0.26 | -0.03 | 2.11 | 1.45 | 0.88 | 0.90
Wind speed (m/s) | -0.45 | 0.01 | 0.85 | 0.69 | 0.80 | 0.80
Averaged stats for urban stations

## Slide 13
Urban VPRM
In order to calculate the biogenic emissions over urban areas, the “others” category is further subdivided into “urban” and “non-urban non-vegetated (NUNV)” areas (snow, barren, sand, water, etc).
Following Hardiman et al., (2017), the dominant vegetation in urban areas is treated as deciduous trees
Inclusion of trees leads to enhanced sequestration of CO2 during daytime and minor addition in nighttime values owing to respiration
The cumulative daily impact of including trees in the urban area equals 12.30 ppm of CO2 sequestered which is around 24 tonnes of CO2 per day
Contribution of 7x11 km urban area in Dublin City
Urban-VPRM estimated CO2 contribution (ppm)

## Slide 14
Model of Urban Network of Intersecting Canyons and Highways (MUNICH)
Emission Data
Meteorological Data
Geographical Data
Photolysis Rate
Background concentration
MUNICH
In-street hourly concentrations
Source: Kim et al., 2018
Simulate subgrid concentrations in the urban canopy
MUNICH consists of two main components:
  Street-canyon - represents the atmospheric processes in the volume of a street.
  Street-intersection - represent the exchange of pollutants between streets.
WRF simulated wind speed and direction, PBL, etc
Street width and length, building height
Traffic flow, speed, vehicle categories, etc

## Slide 15
Gas monitoring unit
https://edgeliot.com/
Station installation across Dublin city
Plan for an urban network of inexpensive GHG monitors to evaluate model simulations and assess zero-carbon policies.
Network to be collocated with existing mobile phone masts and use LoRaWAN to provide real-time data availability.
Monitoring and Evaluation

## Slide 16
High resolution WRF-chem setup with updated datasets at Island scale
Improvement in model simulated meteorology after inclusion of LCZs
WRF-chem captures contribution of biogenic GHGs across Ireland
Conclusions
Implications
Updated emissions at finer resolution
Neighborhood scale analysis for policy implications
Monitoring and Evaluation

## Slide 17
Stewart, I. D. and Oke, T. R.(2012): Local Climate Zones for Urban Temperature Studies, B. Am. Meteorol. Soc., 93, 1879–1900,
Demuzere et al. (2021). LCZ Generator: A Web Application to Create Local Climate Zone Maps. Front. Environ. Sci., 9, 637455, https://doi.org/10.3389/fenvs.2021.637455
Demuzere et al. (2022). A global map of local climate zones to support earth system modelling and urban-scale environmental science. Earth Syst. Sci. Data, 14, 3835–3873, 2022
Mahadevan, et al, 2008: A satellite-based biosphere parametrization for net ecosystem CO2 exchange: Vegetation Photosynthesis and Respiration Model (VPRM) Global Biogeochem. Cycles., 22, GB2005,
Beck, V., T. Koch, R. Kretschmer, J. Marshall, R. Ahmadov, C. Gerbig, D. Pillai, and M. Heimann, 2011: The WRF Greenhouse Gas Model (WRF-GHG) Technical Report No. 25, Max Planck Institute for Biogeochemistry, Jena, Germany
Kim, Y., Wu, Y., Seigneur, C., and Roustan, Y.: Multi-scale modeling of urban air pollution: development and application of a Street-in-Grid model (v1.0) by coupling MUNICH (v1.0) and Polair3D (v1.8.1), Geosci. Model Dev., 11, 611-629, https://doi.org/10.5194/gmd-11-611-2018, 2018.
https://terrainai.com/
THANK YOU
References
https://www.nexsys-energy.ie/