## Slide 1
Air quality and environmental justice implications of deep decarbonization pathways
Dan Loughlin, Chris Nolte, Joyce Kim, and Trinity White (ORISE)
U.S. EPA Office of Research and Development
https://epa.gov/glimpse
Air Quality, Climate, and Energy Session, 2024 CMAS Conference, Chapel Hill, NC, Oct. 21-23rd

## Slide 2: Foreword
Current GLIMPSE Team and Major Contributors
  EPA: Dan Loughlin (co-lead), Chris Nolte (co-lead), Joyce Kim, Kate Crowley, Jia Shi, Uma Shankar, Joe Bronstein (ORISE), Trinity White (ORISE), Heidi Paulsen, Jeff Cole, Julien Isnard, Shannon Koplitz, Colby Tucker, Jia Shi, and Matthew Zwerling
  EPA Collaborators: Shutsu Wong, Bob McConnell, Alex Macpherson, and others
  PNNL: Steve Smith, Maridee Weber, and Rachel Hoesly, and Nathan Wiens
  ARA: Aaron Parks and Yadong Xu
Objectives of this Presentation
  Provide an overview of GLIMPSE and its capabilities to support development of state Comprehensive Climate Action Plans (CCAPs) under EPA’s Climate Pollution Reduction Grant (CPRG) program
Disclaimers
  The views expressed in this presentation are those of the author and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.
  Model results are provided for illustrative purposes only.

## Slide 3: Context
Inflation Reduction Act of 2022
  Climate Pollution Reduction Grant Program (CPRG) administered by EPA
  CPRG provides funds for:
    Climate planning
      Priority Climate Action Plans PCAP (early 2024)
      Comprehensive Climate Action Plans (mid-to-late 2025)
    Implementation of mitigation measures

## Slide 4: How can GLIMPSE support a CCAP?
1. Estimating a GHG inventory
2. Projecting that inventory into the future
3. Estimating the GHG impacts of a single measure or package of measures
4. Identifying strategies for achieving GHG reduction goals
5. Estimating co-reductions of air pollutants
6. Pairing with tools to estimate air quality and health benefits
Capabilities relevant to climate planning:
Notes: SPEAKER: Andrea

## Slide 5: Global Change Analysis Model (GCAM)
Type:
  human-Earth systems simulation model
  state-level resolution (GCAM-USA)
Attributes:
  Open source, freely available
  Operates on Windows, Mac, Unix
  Runtime of 30 minutes to several hours
  Sectoral coverage:
    energy supply and demand, electricity, refining, industry, buildings, transportation, agriculture
  Temporal coverage:
    2015 to 2050 in 5-year increments
  Lead developer:
  Pacific Northwest National Laboratory (PNNL)
GCAM has approximately 40 years of development and hundreds of published applications
Graphic developed by PNNL

## Slide 6: GLIMPSE Software
Developed by EPA
Graphical User Interface for GCAM
Addresses usability barriers
Facilitates:
  Representing policies and measures
  Constructing scenarios
  Executing GCAM
  Visualizing and analyzing results
  Archiving and repeatability
Can be linked to other tools/models to estimate air quality and health impacts
GCAM Long-term Interactive Multi-Pollutant Scenario Evaluator

## Slide 7: Developing a GHG inventory
CO2 emissions by sector, 2020
Chart: 
| Electric | Fuel Production | Industry | Commercial | Residential | Air-Locomotive-Marine | Onroad-Freight | Onroad-Passenger
 | 1362.2744 | 233.9333 | 704.8329 | 205.2715 | 270.896 | 393.2919 | 546.4931 | 932.7069
GLIMPSE represents economic activity and tracks GHG emissions
GHG emissions
CO2:
Based upon fuel-based carbon content
Non-CO2 GHGs:
Included
  Methane (CH4)
  Nitrous oxide (N2O)
  Hydrofluorocarbon gases (HFC)
Sources of EFs
  International Energy Agency
  Emis. Database for Global Atmos. Res.
  Community Emissions Data System
Chart: 
| CO2 | CH4 | N2O | HFC
2020 | 4630 | 341.867 | 512.62 | 76.2
GHG emissions by species, 2020

## Slide 8: Projecting GHGs into the future
Chart: CO2 inventory projection through 2050
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electric | 1362.379 | 1348.839 | 813.3062 | 675.9591 | 679.2644 | 718.2263 | 771.7128
Fuel Production | 233.2 | 226.2333 | 225.1333 | 234.3 | 293.7 | 374 | 451
Industry | 705.5569 | 736.6934 | 786.4538 | 829.2134 | 858.9569 | 847.9233 | 822.9335
Commercial | 205.3154 | 207.8531 | 211.7835 | 214.3149 | 218.3416 | 213.7031 | 216.1726
Residential | 271.0483 | 255.7574 | 228.4409 | 210.1676 | 204.0322 | 201.9486 | 201.8699
Air-Locomotive-Marine | 393.3847 | 396.7421 | 376.7897 | 346.9442 | 335.7616 | 312.89 | 298.6385
Onroad-Freight | 546.6218 | 546.2299 | 519.8071 | 470.7023 | 450.3147 | 419.4835 | 390.3273
Onroad-Passenger | 925.5939 | 771.4842 | 598.4115 | 522.1131 | 479.954 | 446.7006 | 426.89
Electric
Industry
Onroad-Passenger
Onroad-Freight
Air-Locomotive-Marine
Fuels
GLIMPSE simulates evolution of these systems through time
Considerations in making projections:
Population growth and migration
Economic growth and transformation
Climate change
Technology change
Competition for energy, biomass, land and water resources
Other interactions across sectors
Policies that impact these factors

## Slide 9: Evaluating specific reduction measures
GHG reduction measures supported directly in GLIMPSE
Technology subsidies (e.g., for EVs or heat pumps)
Fuel subsidies (e.g., for hydrogen or biofuels)
Technology requirements (e.g., LED bulbs)
Technology capacity (e.g., rooftop solar, offshore wind)
Energy efficiency target for vehicle classes (e.g., MPG target)
Market share targets (e.g., RPS, CES, EVs)
Others that can be simulated in GCAM-USA
Building shell standard improvements
Examples of measures not directly supported in GLIMPSE or GCAM*
Electric distribution grid improvements
Charging infrastructure investments
Other efficiency standards
Cap and trade program (e.g., Regional Greenhouse Gas Initiative)
GLIMPSE has specific “levers” for many GHG reduction measures
* Through share weights, we can simulate changes in bias (e.g., range anxiety)
Notes: SPEAKER: Andrea

## Slide 10: Evaluating packages of reduction measures
Methodology
Modeling approach
Conduct steps relevant for climate planning
  Assess emission reductions from Measures relative to Reference
  Evaluate reductions from each measure individually
  Identify additional opportunities for emission reductions to reach the Net Zero CO2 reduction target in the Goal case
  Estimate co-emitted air pollutant reductions associated with Measures
  Translate these air pollutant emission changes into air quality and health benefits
Scenario design
Reference case
  “Current legislation” assumptions
  Incorporates many major provisions of the IRA (e.g., technology subsidies)
Measures case
  Adds set of GHG reduction measures
  (see next slide for descriptions)
Goal case
  Adds CO2 reduction target to Measures
  Reflects Net Zero target from the recent Energy Modeling Forum 37 study
Notes: SPEAKER: Andrea

## Slide 11: Evaluating packages of reduction measures
The Measures case includes the following:
Power Sector
80% RPS by 2050
Rooftop solar output grows to 1 exajoules (EJ) by 2050
Offshore wind output grows to 3 EJ by 2050
Alternative Fuels Production
IRA hydrogen subsidies are extended through 2050
Buildings
From 2025, all new building appliances are high-efficiency, electric
Onroad Transportation
Light duty: electric sales share grows to 80% by 2050
Freight: electric sales share grows to 50% by 2050
Buses: 100% hybrid or electric sales in 2030, 100% electric from 2035

## Slide 12: Evaluating packages of reduction measures
The Measures case includes the following:
Power Sector
80% RPS by 2050
Rooftop solar output grows to 1 exajoules (EJ) by 2050
Offshore wind output grows to 3 EJ by 2050
Alternative Fuels Production
IRA hydrogen subsidies are extended through 2050
Buildings
From 2025, all new building appliances are high-efficiency, electric
Onroad Transportation
Light duty: electric sales share grows to 80% by 2050
Freight: electric sales share grows to 50% by 2050
Buses: 100% hybrid or electric sales in 2030, 100% electric from 2035

## Slide 13: Evaluating packages of reduction measures
The Measures case includes the following:
Power Sector
80% RPS by 2050
Rooftop solar output grows to 1 exajoules (EJ) by 2050
Offshore wind output grows to 3 EJ by 2050
Alternative Fuels Production
IRA hydrogen subsidies are extended through 2050
Buildings
From 2025, all new building appliances are high-efficiency, electric
Onroad Transportation
Light duty: electric sales share grows to 80% by 2050
Freight: electric sales share grows to 50% by 2050
Buses: 100% hybrid or electric sales in 2030, 100% electric from 2035

## Slide 14: Evaluating packages of reduction measures
The Measures case includes the following:
Power Sector
80% RPS by 2050
Rooftop solar output grows to 1 exajoules (EJ) by 2050
Offshore wind output grows to 3 EJ by 2050
Alternative Fuels Production
IRA hydrogen subsidies are extended through 2050
Buildings
From 2025, all new building appliances are high-efficiency, electric
Onroad Transportation
Light duty: electric sales share grows to 80% by 2050
Freight: electric sales share grows to 50% by 2050
Buses: 100% hybrid or electric sales in 2030, 100% electric from 2035

## Slide 15: Evaluating packages of reduction measures
Simulation of CO2 emission trajectories for Reference and Measures
Chart: Total CO2 emissions by scenario
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
BASE | 5190 | 4630 | 4500 | 3770 | 3530 | 3510 | 3500 | 3510

## Slide 16: Evaluating packages of reduction measures
Simulation of CO2 emission trajectories for Reference and Measures
Chart: Total CO2 emissions by scenario
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
BASE | 5190 | 4630 | 4500 | 3770 | 3530 | 3510 | 3500 | 3510
CNTL | 5190 | 4630 | 4380 | 3530 | 3110 | 2900 | 2660 | 2460
CO2 emission reductions from Measures relative to Reference:
2025: 3%
2030: 6%
2040: 17%
2050: 30%
Cumulative additional emission reductions from Measures through 2050:
16,400 MTCO2

## Slide 17: Evaluating packages of mitigation measures
Results can be decomposed by sector and measure
Chart: Change in CO2 by sector through 2050
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electric | 0.078475 | 3.7953 | 14.7105 | 14.7861 | -74.0494 | -166.125 | -286.414
Refining | -0.73333 | -5.8667 | -11 | -15.7667 | -70.4 | -107.4333 | -147.4
Industry | 0.543 | 4.8223 | 0.44272 | 4.8527 | 56.2154 | 86.2456 | 132.1364
Commercial | 0.03295 | -40.2654 | -67.076 | -96 | -118.8584 | -146.1507 | -152.9702
Residential | 0.11424 | -26.1883 | -45.0409 | -84.1963 | -109.1427 | -132.4069 | -150.3289
Air-Rail-Marine | 0.069597 | -7.1881 | -18.2806 | -36.5318 | -32.7895 | -12.1852 | 17.8652
Onroad-Freight | 0.096495 | -21.7988 | -98.9304 | -168.5054 | -202.6648 | -233.2979 | -253.8961
Onroad-Passenger | -7.1681 | -29.0428 | -29.2506 | -40.1514 | -77.8324 | -152.356 | -249.6071
CDR | 0 | -0.00090244 | -0.04319 | -0.16581 | -0.4946 | -0.17377 | -0.56654
Chart: Cumulative CO2 reductions through 2050
| Buildings | OnroadF | OnroadP | RPS
Cumulative reductions | 6550 | 3750 | 2000 | 3550
Calculated by removing each specific measure from bundle
As tested, other measures had limited impact at national level
Onroad-
Passenger
EV target
Onroad-
Freight
EV Target
Building
electrification

## Slide 18: Identifying strategies for achieving goal
Chart: CO2 emissions vs. reduction goal
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
BASE | 5190 | 4630 | 4500 | 3770 | 3530 | 3510 | 3500 | 3510
CNTL | 5190 | 4630 | 4380 | 3530 | 3110 | 2900 | 2660 | 2460
NZ | 5190 | 4630 | 4250 | 3570 | 2870 | 2180 | 1490 | 799
Comparison of results with Net Zero target in Goal
Reference
Measures
Goal
The modeled measures achieve approximately 45% of targeted reductions
GLIMPSE can be used to gain insights about measures to close the gap
Steps:
Add declining CO2 cap to scenario
Allow GLIMPSE to identify strategy for achieving cap
Assess incremental reductions

## Slide 19: Identifying strategies for achieving goal
Reduction opportunities identified by GLMPSE to fill gap to goal:
Chart: Additional emission changes by sector
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electric | 0.3139 | -47.2592 | 183.2895 | 118.171 | -56.6059 | -275.7641 | -384.4534
Fuel Production | -0.73333 | -10.2667 | -20.9 | 10.2667 | 9.9 | -45.8333 | -97.9
Industry | 2.172 | -18.3425 | -44.3599 | -185.3643 | -362.0238 | -424.2781 | -482.6621
Commercial | -0.9682 | -45.2514 | -78.8573 | -122.4812 | -163.7824 | -202.214 | -213.4479
Residential | -1.0097 | -27.9297 | -48.4591 | -110.1046 | -161.179 | -189.7859 | -214.2769
Air-Rail-Marine | 0.27839 | -21.54 | -40.386 | -70.6197 | -112.203 | -148.3097 | -163.6034
Onroad-Freight | 0.38598 | -32.363 | -106.4029 | -193.5752 | -272.5778 | -320.4743 | -357.9612
Onroad-Passenger | -6.6723 | -35.7466 | -44.0828 | -72.4055 | -159.6832 | -257.6834 | -381.5432
CDR | 0 | -0.0029121 | -0.68743 | -5.6932 | -47.993 | -155.8223 | -449.57
Sector | Short-term (through 2035) | Long-term (post 2035)
Power | Additional wind and solar | Additional wind, solar, nuclear, biomass, CCS
Buildings | Accelerated transition to high-efficiency | Demand reductions
Industry | Application of CCS and biomass-fueled cogeneration | Widespread use of direct air capture and CCS
Onroad transportation | Earlier transition to electric and hydrogen | Expanded use of hydrogen
Nonroad transportation | Earlier transition to electric and hydrogen | Expanded transition to electric, demand reductions
Strategies
Note: CDR represents carbon removal technologies, including direct air capture (DAC)

## Slide 20: Estimating air pollutant co-reductions
Chart: National air pollutant emission trends relative to 2020
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
NH3 | 0 | 0.070352 | 0.12563 | 0.18342 | 0.25126 | 0.32412 | 0.38945
NMVOC | 0 | 0.030769 | 0.0076923 | 0.030769 | 0.069231 | 0.10769 | 0.13846
NOx | 0 | -0.10891 | -0.24134 | -0.30322 | -0.2797 | -0.25248 | -0.22401
PM2.5 | 0 | -0.029851 | -0.08209 | -0.097015 | -0.074627 | -0.059701 | -0.037313
SO2 | 0 | -0.0046948 | -0.29577 | -0.37089 | -0.34272 | -0.32394 | -0.30986
Solid: Reference
GLIMPSE also outputs air pollutants by state and source category
Air pollutants output by GLIMPSE by state, technology, and pollutant:
Ammonia (NH3)
Carbon monoxide (CO)
Nitrogen oxides (NOx)
Sulfur dioxide (SO2)
Fine particulate matter (PM2.5)
Non-methane volatile organic compounds (NVMOCs)
Sources of air pollutant emission factors:
EPA National Emission Inventory
EPA MOVES and IPM models
Various NSPSs
From these results, we can produce emission change factors for use with:
EPA’s Community Multiscale Air Quality model (CMAQ)
EPA’s COBRA air quality and health screening tool

## Slide 21: Estimating air pollutant co-reductions
Chart: National air pollutant emission trends relative to 2020
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
NH3 | 0 | 0.070352 | 0.12563 | 0.18342 | 0.25126 | 0.32412 | 0.38945
NMVOC | 0 | 0.030769 | 0.0076923 | 0.030769 | 0.069231 | 0.10769 | 0.13846
NOx | 0 | -0.10891 | -0.24134 | -0.30322 | -0.2797 | -0.25248 | -0.22401
PM2.5 | 0 | -0.029851 | -0.08209 | -0.097015 | -0.074627 | -0.059701 | -0.037313
SO2 | 0 | -0.0046948 | -0.29577 | -0.37089 | -0.34272 | -0.32394 | -0.30986
NH3 | 0 | 0.067839 | 0.1206 | 0.17588 | 0.22864 | 0.29648 | 0.35427
NMVOC | 0 | 0.031008 | 0.0077519 | 0.023256 | 0.031008 | 0.062016 | 0.077519
NOx | 0 | -0.11881 | -0.2698 | -0.36015 | -0.36881 | -0.3651 | -0.35767
PM2.5 | 0 | -0.037879 | -0.098485 | -0.13636 | -0.15152 | -0.15909 | -0.15909
SO2 | 0 | -0.004717 | -0.30189 | -0.37736 | -0.35849 | -0.33491 | -0.3066
Solid: Reference
Dash: Measures
GLIMPSE also outputs air pollutants by state and source category
Air pollutants output by GLIMPSE by state, technology, and pollutant:
Ammonia (NH3)
Carbon monoxide (CO)
Nitrogen oxides (NOx)
Sulfur dioxide (SO2)
Fine particulate matter (PM2.5)
Non-methane volatile organic compounds (NVMOCs)
Sources of air pollutant emission factors:
EPA National Emission Inventory
EPA MOVES and IPM models
Various NSPSs
From these results, we can produce emission change factors for use with:
EPA’s Community Multiscale Air Quality model (CMAQ)
EPA’s COBRA air quality and health screening tool

## Slide 22: Evaluating air quality and health benefits
Using EPA’s COBRA screening tool
Air quality and health impacts of Measures relative to Reference
 | Population-weighted change in concentration |  | Monetized benefits (2023$s @ 2% discount rate) | 
Pollutant | 2035 | 2050 | 2035 | 2050
Ozone (MDA8 ppbV) | -6% | -10% | $89 billion to $130 billion | $210 billion to $300 billion
PM2.5 (mg/m3) | -2% | -5% |  | 
Notes:
* MDA8 represents the maximum daily 8-hour average ozone concentration, a metric that is used in determining attainment status
** “Low and High values represent differences in the methods used to estimate some of the health impacts in COBRA.” – COBRA Users’ Guide
Change in O3 concentration (ppbV), 2050
> - 0.81
-0.81 to -1.3
-1.3 to -1.6
-1.6 to -1.8
< -1.8
Change in PM2.5 concentration (mg/m3), 2050
> - 0.07
-0.07 to -0.13
-0.13 to -0.19
-0.19 to -0.30
< -0.30
https://epa.gov/cobra

## Slide 23: Investigating environmental justice
Where are these benefits occurring and who is affected?
Combine air quality changes by county with county-level demographic data from EJScreen, the Census, and other data sources.
Factors:
- Percent low income
- Percent people of color
- Land use type (metro, urban, rural)
- Region of country
Use machine-learning approaches such as CART and Random Forest to develop insights.
CART analysis of changes in PM concentrations, 2035
Insights:
PM reductions most sensitive to part of country, with South, then Midwest seeing greatest reductions
In the South and Midwest, the greatest PM reductions tended to be in areas with < 57% people of color, but > 34% low income
Note: We are very early in adding these capabilities to our team but are excited about the insights they can provide.
Trinity White starting to explore these methods

## Slide 24: Take home thoughts
GCAM-USA has the potential to be an important tool in state climate planning
GLIMPSE addresses many of the barriers to running GCAM-USA
GLIMPSE is not a “turnkey” modeling system
  Applications are often an iterative process involving experimentation, learning, and refining assumptions
  Understanding how GCAM works is critical in interpreting results. This requires a commitment of time and effort needed for experimentation
Insights can be gained from big-picture dynamics, but it is always advisable to explore small-scale dynamics
  Why did the model get the result that it did?
  Was this response reasonable?
  Are there real-world factors that were not modeled but which could impact this response?

## Slide 25: Questions?
Contact:
  Loughlin.Dan@epa.gov
  glimpse@epa.gov
To keep up with GLIMPSE developments:
  Visit https://epa.gov/glimpse
    Announcements
    Users’ Guide
    Links to training videos
  Sign up for listserv by emailing glimpse-news-subscribe@lists.epa.gov

## Slide 26: Outline
What is GCAM? What is GLIMPSE?
How can GLIMPSE be used in developing a CCAP?
  Developing a GHG Inventory
  Projecting GHG emissions into the future
  Evaluating impacts of specific GHG mitigation measures
  Identifying additional measures to meet a GHG reduction goal
  Estimating air pollutant emission co-reductions
  Estimating air quality and health benefits
What are the strengths and limitations of using GLIMPSE?
Where to get additional information?

## Slide 27: Evaluating specific reduction measures
D buildings emissions
D other transportation emissions
D industrial emissions
Quaternary (price-induced)
D coal mining emissions
D oil & gas emissions
D biomass production emissions
Tertiary (supply)
D power
emissions
D refinery
emissions
D bio-refinery
emissions
Secondary (fuel production)
Example of dynamics captured in GCAM-USA:
System-wide impacts of vehicle electrification
Measure:
EV subsidy
D onroad
emissions
Primary
Overall?