## Slide 1: Whole Home Electrification Impacts on O3 and PM2.5 in Northeast US – Sensitivity Tests Using EPA 2016 V3 Emission Platform
Yuhong (Ruby) Tian1, Winston Hao1, Eric Zalewsky1, Jeongran Yun1, Alexandra Karambelas2, and Kevin Civerolo1
1Division of Air Resources, New York State Department of Environmental Conservation, Albany, NY
2Northeast States for Coordinated Air Use Management, Boston, MA
CMAS Conference 2024
Oct. 21-23, 2024
Chapel Hill, NC, USA

## Slide 2
Introduction
Parts of the Ozone Transport Region (OTR) continue to experience persistently high ozone levels affecting tens of millions of people.
According to EPA’s National Emissions Inventory (NEI), onsite fuel combustion in residential buildings was responsible for 10% of total NOx emissions in the OTR states in 2020. Residential building-related NOx emissions in OTR states is the fourth largest contributor after on-road vehicles, nonroad equipment and machines, and industrial processes1.
Whole-home electrification (WHE) assumes conversion of space and water heaters, clothes dryers, air conditioners, stoves, and ovens from fossil fuels or electric resistance to heat pumps and electric cooking appliances1.
1NESCAUM and OTC: Residential Building Electrification in the Northeast and Mid-Atlantic: Criteria Pollutant and Greenhouse Gas Reduction Potential

## Slide 3
Methods
Emission Modifications
Model Simulations

## Slide 4: Residential Fuel Combustion (RESFC) SCC’s
Whole-Home Electrification - Methods
Following NESCAUM study using NREL ResStock tool but using EPA 2026 projected emissions
Zero out listed SCCs from nonpt sector over OTR
SCC Code | Category | Type | Fuel Type
2104004000 | Stationary Source Fuel Combustion | All Combustor Types | Distillate Oil
2104006000 | Stationary Source Fuel Combustion | All Combustor Types | Natural Gas
2104007000 | Stationary Source Fuel Combustion | All Combustor Types | Liquified Petroleum Gas (LPG)
2104011000 | Stationary Source Fuel Combustion | All Heater Types | Kerosene
Courtesy to: NESCAUM and OTC: Residential Building Electrification in the Northeast and Mid-Atlantic: Criteria Pollutant and Greenhouse Gas Reduction Potential.

## Slide 5
EGU Adjustment Factors – Electricity Demand Adjustment
Adjusted electricity demand was applied per state and based on current fuel mix.
Adjusted electricity demand was split between heating season and cooling season with water heating spread evenly throughout the year.
Adjustment factors were applied to all model species in the Electric Generating Unit (EGU) SMOKE inline output files.
Adjustment Factors to Baseline EGU Emissions
 | CT, ME, MA, NH, RI, VT | NY | PA, NJ, DC, DE, MD | VA
Summer | 0.96 | 0.94 | 0.92 | 0.90
Winter | 1.56 | 1.51 | 1.18 | 0.87

## Slide 6
CMAQ v5.3.3 Runs with 3 Emissions Scenarios
Emissions Scenarios:
BASE: 2026gf emissions (from EPA 2016V3 Platform) with ERTAC (Eastern Regional Technical Advisory Committee) EGU emissions
RESFC: nonpt emissions reductions only (removed emissions from residential fuel combustion)
RESFC+EGU: nonpt emissions reduction plus EGU adjustments
Simulation Periods:
Winter months: January (shown) and February
Summer months: June and July (shown)

## Slide 7
Results
Emission Modifications

## Slide 8
Monthly Differences in Total NOx Emissions
July
January

## Slide 9
Summary of Emission Changes
Total emission changes by month (unit: tons)
 | NOx |  | VOC_INV |  | PM2.5 | 
 | Jan. | Jul. | Jan. | Jul. | Jan. | Jul.
RESFC minus BASE | -18084 | -517 | -904 | -25 | -897 | -28
EGU minus BASE | +1615 | -699 | +153 | -82 | +216 | -129
RESFC+EGU minus BASE | -16469 | -1216 | -651 | -107 | -681 | -157
Ratio of total emission changes to the total anthropogenic emission by month (%)
 | NOx |  | VOC_INV |  | PM2.5 | 
 | Jan. | Jul. | Jan. | Jul. | Jan. | Jul.
RESFC+EGU minus BASE | -20.4% | -1.8% | -0.6% | -0.1% | -2.3% | -0.5%

## Slide 10
Preliminary Modeling Analysis
Summer: Monthly Difference of Daily Maximum 8HR Average Ozone (MDA8 O3)
Winter: Monthly Difference of Daily Mean PM2.5
RESFC minus BASE
RESFC+EGU minus BASE
Results

## Slide 11
Summer MDA8 O3 Changes
Impacts on elevated summertime ozone were generally small, with localized increases in NYC due to less NOx titration.
Including the adjusted electricity caused additional decreases in regions of elevated ozone.
Base model MDA8 O3 ≥ 60ppb as threshold (i.e., high O3 days)

## Slide 12
Winter PM2.5 Changes
Base model PM2.5 ≥ 9µg/m3 as threshold
Base model PM2.5 ≥ 18µg/m3 as threshold (i.e., high PM2.5 days)
On high PM2.5 days, decreases were larger
PM2.5 decreased by as much as 0.5-1 µg/m3 regionally; >4 µg/m3 in NYC

## Slide 13
Winter NO3 Changes
Base model PM2.5 ≥ 9µg/m3 as threshold
Base model PM2.5 ≥ 18µg/m3 as threshold (i.e., high PM2.5 days)
Much of the decrease in PM2.5 was attributed to nitrate decreases
Nitrate decreased by up to 1.5 µg/m3 on high PM2.5 days
PM2.5 = SO4 + SOIL + OC + NO3 + NH4 + EC + UNSPEC1 + NA + CL

## Slide 14: Conclusions
Whole-Home Electrification
Impacts on elevated summertime ozone were generally minor.
Impacts on PM2.5 were larger during the winter months.
PM2.5 decreased by as much as 0.5-1 µg/m3 regionally; >4 µg/m3 in NYC during high PM2.5 days.
Nitrate (NO3) was the top contributor to PM2.5 decreases.
Disclaimer: The views expressed here do not necessarily reflect the views or opinions of the NYSDEC and NESCAUM.

## Slide 15
Thank you very much!
Questions?
Ruby.Tian@dec.ny.gov
New York State Department of Environmental Conservation

## Slide 16
Extra Slides

## Slide 17
(Base model PM2.5 >= 9µg/m3 as threshold)
Summer PM2.5

## Slide 18
BASE Winter PM2.5
(No threshold)

## Slide 19
Winter PM2.5
Base model PM2.5 >= 9µg/m3 as threshold
All modeled data are used, no threshold

## Slide 20
Winter PM2.5: Individual Components
(No threshold)

## Slide 21
Winter PM2.5: Individual Components
Base model PM2.5 >= 18µg/m3 as threshold