## Slide 1: Improving CMAQ Representation of 2023 Wildfire Air Quality Impacts by Assimilating Satellite NO2 Data
Joshua Kumm1,2, Barron Henderson3, Sergey Napelenok3, Heather Simon3, Zhen Qu2
1 ORISE Fellow at US EPA
2 NC State University
3 US EPA
2024 CMAS Conference, In-Person
The views expressed in this presentation are those of the author and do not necessarily reflect the views or policies of the U.S. EPA.

## Slide 2: Motivation: the 2023 Canadian Wildfires
Last summer, wildfires raged across Canada at an unprecedented scale from May-October
  18.5 million hectares burned (>2.5x previous record)
Frequent smoke plumes produced significant air quality problems across the US

## Slide 3: Rapid Modeling of Fire Impacts
Accurate estimation of 2023 fire emissions crucial to understanding fire impacts to air quality, but not yet available
Rapid modeling efforts such as the Expedited Modeling of Burn Events Result (EMBER) underway at US EPA
  Shown to reasonably capture fire plume extent and downwind ozone formation
  However, high uncertainty remains…
How can we improve representation of the 2023 fires and reduce uncertainty in these modeling efforts?
Notes:   No up-to-date emissions inventories currently available
  CMAQ v5.4 model
  Fire emissions estimated from BlueSky pipeline
  Reasonably captures fire plume extent and downwind ozone formation
  However, high uncertainty remains…

## Slide 4: The Case for Assimilating Satellite NO2
To gain a better understanding of ozone-related fire impacts, we need to start with NO2 at the source
  Fires release large quantities of NOx (including NO2)
  NOx carried via smoke plumes to distant locations, reacting photochemically to form ozone
NO2 observations from the TROPOspheric Monitoring Instrument (TROPOMI) can refine modeled NO2 and ozone concentrations
  Higher spatiotemporal resolution (5.5 km x 3.5 km, 102 min)
  Captures urban-scale air quality on subseasonal timeframe
Notes: NOx is among the major pollutants released in large quantities by wildfires
  Transported long distances in smoke plumes
  Reacts in the atmosphere to form ozone
Accurate estimation of fire NOx crucial to understanding overall wildfire AQ impacts, but no up-to-date emissions inventories are currently available
  Inventories time-intensive, often take years to develop
  US EPA’s early modeling efforts successful, but have high uncertainty

## Slide 5: Gridpoint Statistical Interpolation (GSI)
Gridpoint Statistical Interpolation (GSI) model assimilates satellite chemical data into CMAQ
  Accounts for background error covariance, satellite uncertainty
  Shown to improve agreement between satellite and model
For NO2 assimilation, we introduce an online coupled CMAQ-GSI framework
  GSI simulates ‘new’ NO2 values using 3DVAR assimilation algorithm
  Increment calculated as difference between original and new modeled NO2 values
  Updates NO2 concentrations in CMAQ with increment for areas with available observations
Notes:   First, GSI pauses CMAQ run at top of hour to check for TROPOMI observations
    GSI simulates ‘new’ NO2 values using 3DVAR assimilation algorithm,
    Calculates increment as difference between original and new modeled NO2 values,
    Updates NO2 concentrations in CMAQ with increment
  GSI process is complete, and CMAQ run resumes

## Slide 6: NO2 Assimilation Modeling Setup
Two CMAQ v5.4 model simulations are performed over the 2023 North American fire season: a ‘NOASSIM’ run, and an ‘ASSIM’ run
  NOASSIM - base simulation
  ASSIM - with GSI NO2 data assimilation
Both model runs use 2023 EMBER inputs/specifications
  April 11 - September 30, 2023 (10 day spinup)
  36US3 domain, 35 vertical layers
  NACC meteorology, NASA GEOS-CF IC/BCs
  2018 avg anthropogenic, 2023 BlueSky preliminary fire emissions
Notes: ‘NOASSIM’: a base model run with CMAQ-GSI NO2 data assimilation turned ‘off’,
‘ASSIM’: CMAQ-GSI NO2 data assimilation turned ‘on’, occurring occasionally at hours with available obs

## Slide 7: Case Study Overview
We sampled one ‘normal’ time period, and two multiday fire events to investigate:
Non-Fire Event: April 11-15, 2023
Fire Event #1: June 3-7, 2023
Fire Event #2: July 12-16, 2023
We use three metrics to evaluate model performance:
Comparison of TROPOMI and CMAQ NOASSIM NO2 Vertical Column Densities (VCDs)
NOASSIM and ASSIM model-simulated NO2 Differences at lower, mid, and upper levels
NOASSIM and ASSIM model-simulated O3 Differences at lower, mid, and upper levels

## Slide 8: Non-Fire Event: April 11-15, 2023 Left: TropOMI vs CMAQ NO2 Vertical Column Densities (VCDs) Right: ASSIM vs. NOASSIM NO2 Differences at 1000, 500, and 200 mb
TropOMI - CMAQ
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 9: Non-Fire Event: April 11-15, 2023 ASSIM vs. NOASSIM Surface O3 Differences
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 10: Fire Event #1: June 3-7, 2023 Left: TropOMI vs CMAQ NO2 Vertical Column Densities (VCDs) Right: ASSIM vs. NOASSIM NO2 Differences at 1000, 500, and 200 mb
TropOMI - CMAQ
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 11: Fire Event #1: June 3-7, 2023 ASSIM vs. NOASSIM Surface O3 Differences
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 12: Fire Event #2: July 12-16, 2023 Left: TropOMI vs CMAQ NO2 Vertical Column Densities (VCDs) Right: ASSIM vs. NOASSIM NO2 Differences at 1000, 500, and 200 mb
TropOMI - CMAQ
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 13: Fire Event #2: July 12-16, 2023 ASSIM vs. NOASSIM Surface O3 Differences
Notes: -Spatial structure of NO2 changes in the model correlates to the absolute differences we saw between TROPOMI and NOASSIM CMAQ
-Magnitude
-Broad ozone increases in areas where NO2 was raised

## Slide 14: Conclusions
TROPOMI retrieved NO2 columns are significantly lower than CMAQ at fire plume locations
In areas not experiencing wildfire impacts, broad areas exist where TROPOMI > CMAQ, indicating CMAQ EMBER anthropogenic NOx emissions may be low
Inter-run comparison shows that GSI improves agreement between CMAQ and TROPOMI NO2
  Indicates validity of CMAQ-GSI system
  GSI implementation has direct impact on CMAQ representation of ozone
  Note: this claim has yet to be independently verified
Notes:   Present in both case studies
  Reflected in NOASSIM and ASSIM run comparison
Valdiity - assimilations are “in the right direction”
Explain TROPOMI senesitivty issue - in areas of thick smoke, TROPOMI top-down measurements cannot properly see the surface, which can result in improper column approximation, i.e., “lower” values interpolated than we would expect based on limited info

## Slide 15: Next Steps
Further investigation of near-fire discrepancies in TROPOMI and CMAQ NO2
  Currently unclear whether this is a TROPOMI sensitivity issue, CMAQ overestimation of fire emissions, or something else
  Looking into possible artifacts within the near fire retrievals
Evaluation of model performance with respect to in situ observations
  Compare NOASSIM/ASSIM CMAQ performance to available AQS data for O3
  Perform quantitative analysis and compute revealing statistics
  Determine whether the assimilation induced changes are in line with other observations
With this work, we seek to inform 2023 rapid modeling efforts, and inspire policy action!