## Slide 1: Addressing PM2.5 Exposure Disparities: High-Resolution Modeling and Health Assessment for Environmental Justice Across the Contiguous U.S. (CONUS)
Kai Fan, Zhen Qu
23rd annual CMAS Conference
October 22, 2024
Notes: More self introduction

## Slide 2
Motivation
With the rapid development of the economy and industry, PM2.5 has been significantly impacting human health, especially after industrial revolution
Based on data in 2015, ambient PM2.5 was the fifth-ranking mortality risk factor (Cohen et al., 2017)
(https://www.britannica.com/event/Great-Smog-of-London)
Great Smog of London
Dec. 5 – Dec. 9, 1952
4000+ Deaths
Notes: Pm2.5 are particles that are 2.5 μm or less in diameter

## Slide 3
Motivation
PM2.5 measurement sites over CONUS
The U.S EPA Air Quality System (AQS) has been monitoring air quality since 1970s. Until 2023, there has been 1000+ sites measuring PM2.5
PurpleAir, a low-cost sensor system, serves as an important supplement for PM2.5 monitoring. There has been 16000+ sensors until 2023.
Predominantly White Census Tract
Notes: AQS sites at 22% counties
Only 21% PurpleAir sensors are in disadvantaged communities (including low income, low employment status, low housing cost, and high pollution exposure)
Climate and Economic Justice Screening Tool (CEJST) defines census tracts as disadvantaged communities based on a combination of variables including low income, low employment status, low housing cost, and high pollution exposure.
Air pollution significantly impacts human health, but air quality monitoring is predominantly focused in high-income, predominantly white areas. This disparity leaves disadvantaged communities unaware of their exposure levels and associated health risks, we want to improve air quality modeling to address this issue.
Add map of residence of different groups

## Slide 4
Chemical transport model (CTM)
  Pros
    Based on physical chemical mechanisms
  Cons
    Large input data
    Heavy computational burden
    Uncertainty
Air quality modeling
Machine learning model
  Pros
    Efficiency
    Adaptability
  Cons
    Usually use CTM model output for training
Develop a machine learning model without relying on CTM simulations to predict high-resolution PM2.5
Notes: Highlight the “not relying on ctm”

## Slide 5
What are the factors that are associated with PM2.5?
Meteorology
Land use
Aerosol optical depth (AOD)
goes-r.gov
Extinction of light passing through atmosphere
(Chen et al., 2020)
(Zhang et al., 2021)
Notes: Cloud snow/ice

## Slide 6
U-Net architecture
using partial convolutions
AOD from
MERRA-2 reanalysis
Training
AOD from
GOES-R
Prediction
Features
ERA5 Meteorology
Gap-filled AOD
Geographical data
Population data
Training
Random Forest
PM2.5 observations
Target
PM2.5 over CONUS
Population
Premature deaths
Modeling framework
1. AOD gap-filling
2. PM2.5 prediction
3. Health assessment
Prediction
Liu, et al., 2018.

## Slide 7
AOD Gap-filling
U-Net architecture
using partial convolutions
AOD from
2023 MERRA-2 reanalysis
Training
X, Y, MASK, VALMASK
AOD from
GOES-R
Prediction
Format the data into multiple 36 * 500 * 800 patch
For daytime
Randomly mask 50% data
For nighttime
Mask 100% data
Gap-filled AOD
This U-Net-like model vs ordinary U-Net
Better for irregular holes in image inpainting
More efficient
Smooth boarder
(Wang et al., 2021)
Ordinary U-Net Architecture

## Slide 8
An example of AOD gap-filling
2019-09-10 19UTC (15EST)
AOD Gap-filling
GOES-West
GOES-East
The gap-filling process may require up to 10 iterations, but it only takes a few minutes to complete.

## Slide 9
AOD Gap-filling
Evaluation of gap-filled AOD against ground-based measurements from AERONET network During 2019 – 2023
Before Gap-fill
After Gap-fill
Although the correlation coefficient (R) decreased by ~0.1 after gap-filling, the model retains the mean bias and RMSE

## Slide 10
Features
Training
GPU-based
Random Forest
PM2.5 observations
Target
Prediction
PM2.5 over CONUS
Geographical data
Population data
ERA5 Meteorology
Gap-filled AOD
PM2.5 prediction
Surface T, U-wind, V-wind, PBL, Solar radiation
Land cover, terrain height
AQS, PurpleAir
(Caquilpan et al., 2019)
Example of Random Forest
Notes: Compared to CPU-based Random Forest, GPU-based Random Forest could accelerate the model training up to 45x

## Slide 11
PM2.5 prediction
Spatial-based cross-validation
Annual
Monthly
Daily
Compared to AQS / PurpleAir measurements, this ML model provides accurate PM2.5 in daily, monthly and annual scale (R2 > 0.7, mean bias ~-0.07 μg/m3, RMSE < 4 μg/m3)
Observation
ML prediction
PM2.5 concentration (μg/m3)

## Slide 12
PM2.5 prediction
Spatial-based cross-validation
Annual
Monthly
Daily
PM2.5 predictions using spatiotemporally weighted deep forest (SWDF, Wei et al., 2023).
Our model outperforms the SWDF deep learning model with higher R2 and lower bias and error

## Slide 13
Health assessment of 50 most populous counties in the CONUS
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
35
36
37
38
39
40
41
42
43
44
45
46
47
48
49
50
……
Relative Disparities
# of Premature Deaths
Distribution of Highest Relative Disparity by Group Across 50 Counties
At only 3 out of 50 counties, the relative disparity of NH-White population is higher than other groups
Relative Disparity =
# of Premature Death =
P Population
BRO Baseline mortality rate
AF(z) Attribution fraction of a pollutant exposure z

## Slide 14
Health assessment of Maricopa County, AZ
Census-tract-level
Annual mean PM2.5 in 2022
Percentage of NH-White
in total population
Percentage of Hispanic
in total population
The largest difference of relative disparities between NH-White and Hispanic population occurred in 2022
PM2.5 levels in downtown Phoenix are higher compared to surrounding areas, where the Hispanic population is the predominant group.
In contrast, PM2.5 levels are significantly lower in northern Maricopa County, where the NH-White population predominantly resides.
American Indian are exposed to high PM2.5 level in the southern county.
Percentage of American Indian
in total population

## Slide 15
Health assessment of Wake County, NC
Census-tract-level
Annual mean PM2.5 in 2022
Percentage of NH-White
in total population
Percentage of NH-Black
in total population
Wake County, the most populous county in North Carolina, is one of the counties with the smallest disparities in relative PM2.5 exposure across racial groups
Similar to Maricopa, AZ, more people of color live in downtown Raleigh, while NH-White residents primarily live in the northern and southeastern parts of Wake County
due to relatively low and consistent PM2.5 levels (6.6–7.2 μg/m³) across the county, the difference in relative disparity between NH-White and NH-Black residents is minimal, at just 0.0018.
Notes: Now where we live

## Slide 16: Summary
We developed a hybrid machine learning framework to predict PM2.5 across CONUS using gap-filled AOD measurements, meteorological reanalysis data, and other publicly accessible predictors. Our model achieved an R2 of 0.76 when compared to annual averaged PM2.5 ground observations.
The model is computationally efficient, does not depend on CTM outputs, and avoids the associated CTM uncertainties.
We assessed PM2.5 exposure from 2019 to 2023 in the 50 most populous U.S. counties. Non-Hispanic (NH) Black and Hispanic populations face higher PM2.5 exposure than NH White populations, with relative disparities exceeding the average in 33 and 43 counties, respectively.
Maricopa County has the largest relative disparity between NH White and Hispanic populations due to higher PM2.5 levels in downtown Phoenix, where many Hispanic residents live. In contrast, Wake County, NC, demonstrates more balanced PM2.5 exposure across racial groups, with lower PM2.5 levels.

## Slide 17: Thanks
Any questions?