## Slide 1
Katie Tuite1, Chris Emery1, Ling Huang1,2, Pradeepa Vennam1, Greg Yarwood1
1Ramboll
2School of Environmental and Chemical Engineering, Shanghai University
CMAS Conference 2024
Evaluating updated secondary organic aerosol (SOA) formation schemes in CAMx
Funding from:

## Slide 2: Motivation
Annual PM2.5 National Ambient Air Quality Standard (NAAQS) reduced from 12 μg/m3 to 9 μg/m3
PM modeling needed for State Implementation Plans (SIP)
Secondary organic aerosol (SOA) is a major component of PM2.5 in many regions
Differing SOA schemes can affect air quality forecasts and assessments
Purpose: Review and update the CAMx SOA treatment to better guide effective PM2.5 SIP strategies
Source: Final Reconsideration of the National Ambient Air Quality Standards for Particulate Matter (PM) | US EPA
Tuite CMAS2024

## Slide 3: SOA treatment in models
Two-product scheme and Volatility Basis Set (VBS) are common approaches
CAMx SOAP is a modified two-product scheme: high, low, and non-volatile products
Tuite CMAS2024
CG = condensable gas; = CG yield; Y = SOA yield; C* = saturation vapor pressure; COA = organic aerosol concentration
(I/VOC)

## Slide 4: Comparison of instantaneous (nonaged) SOA yields at 298 K
8 SOA schemes in 5 models
Calculated Y with scheme-specific parameters (, C*)
Anthropogenic, biogenic, and IVOC precursors
Differences in:
    Magnitude of Y
    Trend with COA
    Impact of NOx
    Treatment of IVOC
Tuite CMAS2024

## Slide 5: Updated CAMx SOA schemes tested using box models
Structure of SOAP maintained but SOA yield parameters updated in 3 test schemes
Curves fit to AERO7/CRACMM SOA yield data using SOAP C* values
Assumes all SOA formed is non-volatile; parameters based on multi-model averages and work by Seltzer et al., 2021
    Parameters that emulate
    CMAQ AERO7
    (“E-AERO7”)
    Parameters that emulate
    CMAQ CRACMM
    (“E-CRACMM”)
    Parameters that emulate a
    “SIMPLE”-style scheme
Tuite CMAS2024

## Slide 6
CAMx box model tests – scaled emissions runs
SOA response to varying anthropogenic VOC and NOx emissions
Similar response for SOAP, AERO7, SIMPLE
    SOA decreases as NOx increases
CRACMM behaves differently from others
    ‘Ridgeline’ is at higher NOx factor (SOA increases before it decreases)
Base case (1,1)
Dallas-Fort Worth: SOAP
Dallas-Fort Worth: E-CRACMM
Dallas-Fort Worth: E-AERO7
Dallas-Fort Worth: SIMPLE
Tuite CMAS2024

## Slide 7
CAMx box model tests – reduced NOx runs
 | SOAP | E-AERO7* | E-CRACMM* | SIMPLE
 | Base - 50% NOx | Base - 50% NOx | Base - 50% NOx | Base - 50% NOx
Dallas-Fort Worth |  |  |  | 
ASOA | 9.6% | 1.9% | 3.5% | 0.6%
BSOA | 12.2% | 0.4% | -10.7% | 2.4%
Total SOA | 10.3% | 1.6% | -2.5% | 0.9%
San Antonio |  |  |  | 
ASOA | 3.7% | 2.1% | 2.3% | 1.0%
BSOA | 3.7% | 0.3% | -10.0% | 1.8%
Total SOA | 3.7% | 1.8% | -3.2% | 1.1%
Tyler/Northeast Texas |  |  |  | 
ASOA | 4.4% | 9.9% | 1.0% | 8.5%
BSOA | -4.1% | -6.2% | -12.6% | -4.4%
Total SOA | -2.5% | -1.8% | -11.0% | -1.5%
Difference in average SOA concentration (μg/m3) between base run and 50% NOx emission reduction run
ASOA = anthropogenic SOA; BSOA = biogenic SOA
*E-AERO7 and E-CRACMM have limited aging representation
Unique CRACMM behavior due terpene yield

## Slide 8: Advantages of SIMPLE scheme
Straightforward to implement
Potential to improve computational efficiency (especially with CAMx’s source apportionment probing tools)
Behaves more predictably without nonlinearities present in other schemes
Ability to calculate emission-weighted SOA potential of precursors
Dallas- Fort Worth
Tuite CMAS2024

## Slide 9: CAMx SOAP updates
SOAP3 released with CAMx v7.3 (June 2024)
Two options for SOA yield parameters
    COMPLEX – based on E-AERO7 implementation
    SIMPLE – non-volatile SOA
Additional updates (not discussed in this presentation)
    POA evaporation
    SOA from heterogeneous uptake of glyoxal and methylglyoxal
Details provided in User’s Guide at www.camx.com
Tuite CMAS2024

## Slide 10: Next steps
Update CAMx’s Particle Source Apportionment Technology (PSAT) probing tool for use with SIMPLE scheme
Update IVOC emission speciation to differentiate between Volatile Chemical Products (VCP) and IVOC
Thank you!
ktuite@ramboll.com
www.camx.com
Tuite CMAS2024

## Slide 11: Extra slides

## Slide 12
CAMx box model tests – scaled emissions runs

## Slide 13: Emission-weighted SOA potential
Dallas
Tyler